README, prepared by W. Menke, 4 June 1992

South Iceland Refraction Experiment of 1990

This directory contains seismogram data for the South Iceland
Refraction Experiment that was conducted by the Lamont-Doherty
Geological Observatory of Columbia University (Palidases, NY)
and the National Energy Authority of Iceland during July through
September, 1990.

The experiment design is a linear profile of 210 receiver points
and 11 shot points crossing the Western Volcanic Zone and
South Iceland Seismic Zone of south Iceland.  The 11 shot points
are named ak, bf, hf, sv, tv, uv, hv, ta, yr, er, jl, from
west to east. The receiver points were in five deployments,
a01, a02, ..., e45, e46, from west to east.

The data are archived in LDGO 'AH' VERSION 1 format, as single
trace files in shot point gather directories.  Hence the file
ak/statlink/a01.z is the vertical component of shot point ak, receiver
point a01.  The suffices .r and .t refer to the radial and
tangential components of the horizontal, respectively.

The AH header have been filled in as best as possible, except that
the poles-and-zeroes of the instrument response has been left
blank.

The LDGO AH programs have been included in the 'ah directory
so that some record of the format of the data is preserved
along with the dataset.  The program ah2asc will produce an
ascii dump of the files.

Instrumentation consisted of:
	15 REFTEK Model 72A digital recorders with AMP01 electronic
		modules and Omega radio timing (from IRIS), with
		cable reels to allow two widely separated
		geophones
	22 Sintrex PRS-4 digital recorders with timing set from
		a Nonometrics Field Clock that was synchronized
		to Omega (10 from LDGO, 5 from IRIS, 5 from USGS,
		3 from U. Colarado).
	Mark Products L22-D and L28 3-component geophones (15 from
		Lamont, the rest from IRIS).

Shots were dynamite in water (ocean, lakes, rivers) and were timed by
a Nanometrics Field Clock synchronized to Omega.

Shot and station locations were determined by either or both:
	GPS location with a Trimble Transpack GPS hand-held
		receiver (Selected availability was off during
		the experiment)
	Measurement from a geodetic quality air photograph.
	Location errors are believed to be about 20 m

The file shot.tab describes the shots:
	column 1: shot name
	columns 2 and 3: Icelandic Lambert coordinates
	column 4: elevation above sea level, meters
	column 5: depth in water, meters
	column 6: kg of dynamite
	column 7: shot time
	column 8: comment, including deployment number

The file stat.tab describes the receiver points:
	column 1: receiver point name
	columns 2 and 3: Icelandic Lambert coordinates
	column 4: elevation above sea level, meters
	column 5: (for internal use)
	column 6: instrument type, r=REFTEK 72A p=PRS-4

Results of the analysis of P wave travel times, including
measurements of crustal thickness from Moho reflections and
tomograhic inversion of upper crustal structure are described
in:

Bjarnasson, I., W. Menke, O. Flovenz and D. Caress, Tomographic
Image of the Spreading Center in Southern Iceland, submitted
to J. Geophys. Res., 28 May 1992.

The authors are currently in the process of performing a tomographic
inversion for shear wave velocity, using this data set.