File Name GSEINTRO.DOC

		       INTRODUCTION TO GSETT-2
		       =======================
			     January 1992

The  Group of  Scientific  Experts  Second  Technical  Test (GSETT-2)   was an
ambitious experiment in terms of the international nature of its participants,
the volume of data collected and  exchanged, the analysis procedures followed,
and the time   schedule under which the experiment   took   place.  In   rough
numbers, the  GSETT-2  archives contain  parametric  data  from 3,000  seismic
events as recorded by 60   globally-distributed stations over a 42-day  period
from  22 April through 2  June 1991.  Evaluation  of the success of GSETT-2 by
the Group's delegations and working groups is still underway. The data on this
two-volume set  of CD-ROMs promise to provide  a  foundation for the continued
evaluation of  GSETT-2, but also  promise to be an  important resource for the
broader seismic research community.

In this document,  we provide an overview   of GSETT-2  that  aimed at  giving
potential users of the CD-ROMs who are unfamiliar  with the test a perspective
on the origins and intent of  the  data.  We review  the concepts, operational
logistics, analysis procedures, and results.  Note  that  what we provide here
is  only a very brief summary  of the information  contained in many documents
published by the Group of Scientific Experts and  its national delegations. We
strongly encourage  users  to reference these documents for   details.  Please
contact  your national GSE delegation (see  CONTACTS.DOC file) to  request GSE
documentation.


		      1.0 HISTORICAL BACKGROUND

The Ad Hoc Group of Scientific Experts to Consider  International Co-operative
Measures to Detect and Identify Seismic  Events (GSE)  was established in 1976
by what is now the Conference on Disarmament.  Through many conference reports
(starting with the first, CCD/558, 1978), the GSE defined  the concepts for an
international system of seismic data exchange capable of providing all parties
equal access to data useful for monitoring a  limited or comprehensive nuclear
test-ban  treaty.   The concepts  included  a   global network  of   about  50
high-quality seismic stations, capable of supplying both parametric  "Level I"
data (arrival  times,  amplitudes, periods,  etc.)   and digital waveform data
("Level  II") to  a system of  data centers  for  processing and dissemination
according  to  strict procedures. During the first  large-scale  test of these
concepts in 1984 (the Group of Scientific  Experts  Technical Test, or GSETT),
parameter data  were routinely  sent  to International Data Centers  for event
location processing. Waveform data were to be available  on request, but never
exchanged routinely (CD/720, 1986).

Rapid developments in  seismic    acquisition systems,   communications,   and
computer processing led the GSE to propose an expansion of the  global system.
In particular, there was a concensus that the  routine exchange and processing
of seismic waveforms  in conjunction with  parameter data  could significantly
improve the  efectiveness  of the system.    A second  technical test  (called
GSETT-2),  including  several warm-up  phases  and   a full-scale   test,  was
conducted during 1990  - 1991 to evaluate  these and other new  concepts.  The
data on the GSETT-2 CD-ROMs are from the full-scale test of GSETT-2, with data
collected between 22 April and 2 June 1991.


		 2.0 OPERATIONAL CONCEPT AND SCHEDULE

The GSE  system for the full-scale test  included National  Data Centers (NDC)
which collected and forwarded seismic data  to four Experimental International
Data Centers (EIDC) in Canberra, Moscow, Stockholm, and Washington.  The EIDCs
followed agreed procedures to produce and dispatch a  series of  seismic event
bulletins  with the objective   of obtaining  a  unified final  bulletin  that
represents the best hypotheses of the four.  A difficult requirement  was that
all data centers adhere to a demanding and rigid schedule in which they had to
process the data from several "Data Days" simultaneously. Days 0 - 7 represent
the days in the eight-day GSE processing cycle relative to each given data day
(Day 0).  Instructions  for the test,   including message formats,  processing
procedures, and schedules are given in CRP 190/Rev 4, 1990.

On Days 0 - 1, the NDCs were responsible  for recording seismic data  from one
or more stations run by their country, then for analyzing these data to detect
and  identify seismic  phases, measure the required parameters  or features as
specified   by  CRP  190  (arrival  time,  amplitude, period,   etc.), and, if
possible, use national means to locate events.  Measured detection parameters,
accompanying waveform segments, and  event    solutions  were dispatched   via
various   communications channels    (e.g., by direct     satellite links   to
communications nodes, electronic mail, Internet links, etc.) to all four EIDCs
in strictly-formatted messages by the end of Day 1.

EIDCs continuously received,  parsed, and archived  the incoming  data.  Daily
logs of all messages sent and received were  exchanged by  the EIDCs to assure
that  their databases were identical.  By the end  of Day 2 EIDCs computed and
dispatched  an  Initial Event List (IEL) prepared  following strict rules from
the parameter data by an automatic  association  program.  A primary  focus of
GSETT-2 was to determine the value of analyzing  waveform data  in conjunction
with seismic parameters  for producing an  improved seismic  bulletin, and the
EIDC did this  analysis during  Days 3  - 6.  EIDCs could request supplemental
data from  NDCs to better  define hypothesized  events.  A  Current Event List
(CEL) showing the   current state   of   each  EIDC's analyzed  bulletin,  was
exchanged daily as a means of communicating the current thinking of  each EIDC
on the events of the Data Day.  A  final CEL  was dispatched from each EIDC at
the end  of  Day 6, and  these were  combined  using  prescribed rules  by the
"responsible EIDC" (a rotating  assignment) to form the  Final  Event Bulletin
(FEB) for dissemination to all data  centers.  All parameter and waveform data
had   to be readily    accessible  at each data  center   from  Day  0  -  15.
Representative of the demands of the schedule is  the fact the  an EIDC had to
compile and dispatch up to six event lists and bulletins in a single day.


		    3.0 NDC PROCESSING PROCEDURES

The most important procedures  at  a GSE National Data  Center that pertain to
the   data on  these  CD-ROMs are  those  governing the  reporting  of seismic
waveform and parameter   data.  Details  on   these procedures   are given  in
Appendices A and C, respectively,  of CRP 190/Rev  4 (1990). Modified excerpts
of these appendices are given at the end of this file.


		    4.0 EIDC PROCESSING PROCEDURES

The most important procedures at  a GSE Experimental International Data Center
that pertain to the data on these CD-ROMs  are those governing the compilation
of  the Initial  Event List  (IEL), Current Event  List (CEL), and Final Event
Bulletin (FEB). Details on these procedures are given  in Appendices  B, F and
J, respectively,  of   CRP   190/Rev 4  (1990).  Modified   excerpts  of these
appendices are given at the end of this document.


		5.0 PRELIMINARY SEISMOLOGICAL RESULTS

GSETT-2 was comprised of 42 data days starting from 22 April  1991 and running
through 2  June 1991.  The last FEB  was scheduled to be  dispatched on 9 June
1991.  Below,  we  provide some rough    statistics that  will  be  useful for
assessing the content of  the GSETT-2 CD-ROMs.   These statistics are from the
Washington EIDC database and are rounded to the nearest one or two significant
digits.   These statistics will be  further  refined and presented  to greater
precision as the GSE evaluation proceeds.

NETWORK
  EIDCs						4 data centers
  NDCs				     	       35 data centers
  Stations			     	       60 stations
    arrays				       12 stations
    1 or 3 component			       48 stations
  Min and Max Latitude of stations	      78S lat. to  77N lat.
  Min and Max Longitude	of stations	     160W lon. to 175E lon.

PHASE ARRIVALS
  Number   	  	  	  	   66,000 phases
  % Associated			               39 %

WAVEFORMS
  Segments				   85,000 segments
  Volume				      1.2 Gbytes

EVENTS
  Washington CEL (WASCEL directories)	    2,700 events
  FEB (GSEBULL directories)		    3,700 events





Please forward questions and comments on any related subject to:

	Dr. Steven Bratt, Mr. David Bonnett, Mr. David Corley
	  Washington Experimental International Data Center
		      Center for Seismic Studies
		  1300 North 17th Street, Suite 1450
		       Arlington, VA 22209 USA
		       Telephone: 703-276-7900
			Telefax: 703-243-8950
			   Electronic Mail:
  bratt@seismo.css.gov, bonnett@seismo.css.gov,corley@seismo.css.gov
				   


===========================================================================
===========================================================================




		    EXCERPTS FROM CRP 190/REV 4 APPENDICES
 





NDC PROCEDURES: WAVEFORM TIME SEGMENTS TRANSMITTED 
       FOR EACH DETECTED SIGNAL
(Excerpt from Appendix A, CRP 190/Rev 4, 1990)

During  GSETT-2, short-period  waveform   time   segments will  be   regularly
transmitted by NDCs for each  detected seismic signal.    The length of  these
segments will be 120 seconds of vertical  component  data, starting 30 seconds
before a detected arrival.  Array  stations  will send such segments from both
the   best beam and   from one sensor.   For local  and   regional events, the
waveform will consist of short-period vertical waveform segments commencing 30
seconds before P    and  continuing  for 30   seconds after the  last  clearly
discernable phase.

The regular transmission  of long-period data  for detected Rayleigh  waves is
optional,  but  as  many NDCs  as possible are   urged  to attempt this during
GSETT-2.   For those NDCs  that will  do  so, time segments  will be regularly
transmitted for  all detected  Rayleigh waves,  whether  or not  such Rayleigh
waves  can be  associated with events whose P  waves have been  detected.  The
length  of  these segments will  be  30 minutes  of vertical  component  data,
starting 5 minutes before the estimated onset time of the Rayleigh waves.

Abbreviated reporting  of waveform  data would be permitted  during especially
large sequences of local earthquakes, rockbursts and quarry blasts, similar to
the abbreviated  reporting of parameter  data described in Appendix  C. If the
number  of events exceeds about 10  per day from  the same  location, waveform
time segments may   be  reported  only for  the largest  event  each day.  The
parameter message will give the number of similar events on that day.


NDC PROCEDURES: LEVEL I PARAMETERS TO BE REPORTED FROM
       THREE-COMPONENT STATIONS AND ARRAY STATIONS
(Excerpt from Appendix C, CRP 190/Rev 4, 1990)

Parameter reports  from  each station  contain  only  information required  to
permit IDC's to  locate seismic  events, determine the focal depth,  determine
Mb, and determine Ms when associated  Rayleigh waves are  detected.  A summary
of the wave types and the parameters to be reported is given in Table C.1.

The basis for the definitions of the parameters is the set of instructions for
extraction of level 1  data  described in earlier GSE  CD  documents (CCD/558,
CD/43 and  CD/448) and used  for the  GSETT  (Conference Room Paper 131/Rev1).
The definitions  as  presented here apply to   extraction by an   analyst  and
include  the experience   gained during  the   GSETT (documented in   CD/720).
Definitions for procedures based on automatic  processing, including those for
back azimuth, angle of incidence,  as well as level  of rectilinearity have to
be further developed and tested.

For   amplitude and period  measurements,  the stated  precisions  may not  be
achievable at all stations,  and in this  context it should be noted  that the
reporting formats (see Annex D1) are `free' format and permit some latitude in
precision of reported values.  Two significant figures are considered adequate
for both amplitude and period.

C.1	First arrival time of P-wave

On a visual record a first arrival time is defined by a change in amplitude or
phase.  The time reading is given in hours, minutes, seconds,  and tenths of a
second in Universal Coordinated Time  (UTC).   If the time is uncertain (clock
problems) by   more than 0.05  second,  it  must  be reported  in  qualitative
remarks.  The first arrival should always  be identified,  if possible, by one
of standard symbols.  The   symbols (phase codes)  used by  the  International
Seismological Center are recommended.

Because of the high accuracy of time measurements the  problem of instrumental
time delay must be noted.  As an example,  for WWSSN  (World Wide Standardized
Seismograph Network) SP instruments at 1 Hz, phase delay is about  0.3 seconds
and group  delay  time is  about   0.4 seconds.  Corrections for these  delays
should be made before reporting arrival times.

C.2	First Motion Sign and Clarity

Direction (or sign) of  the first motion  on vertical short-  and  long-period
instruments should be   reported.   For  complicated or   weak  signals,   the
direction  of the first  motion  may  be in  doubt; if so,   it is not   to be
reported.  Theoretically the first onset should have the  same  sign on short-
period (SP) and long-period (LP) instruments.  However, due to different noise
conditions, frequency  response and magnification of  SP and LP recordings the
first motions do not need to agree, particularly for multiple  events starting
with weak arrivals.    In the  case of  a  discrepancy in  the  directions the
reasons should be checked by the operator before the information is reported.

The following first motion notations should be used:

C	-	SP compression (Up)
D	-	SP dilatation (Down)
U	-	LP compression
R	-	LP dilatation

The  clarity parameter is  used to indicate whether a  recorded seismic signal
represents a clear onset.  If the  signal  onset can be  identified within +/-
0.2 seconds for P waves or +/- 1 second for S waves, the clarity notation I is
used, while if the onset identification is less accurate, the clarity notation
E is to be  used.  The  clarity parameter Q is to  be used for  initial phases
whose onset cannot be determined to better than 1 second accuracy.

C.3	Time of Maximum P-wave Amplitude

This time corresponds to  the maximum amplitude measured  in the  interval 0-6
seconds after the arrival of the P-wave.   In case of large teleseismic events
this interval would be extended to 20 seconds.

C.4	Associated Amplitude

The  amplitude of  the first  phase  is to be   determined from maximum  trace
amplitude within the  first six seconds, corrected to  ground motion using the
measured  period and the     instrument response  curve.  Trace amplitude   is
measured on  the vertical component as  the center-to-peak deflection from the
median  line or may be  obtained by taking  one half  of  the peak-to-  trough
deflection of  symmetrical  waves.   The  ground   amplitude  is reported   in
nanometers to a precision of 0.01  nanometres.  Since the  upper limit  for an
absolute  calibration of  seismographs  is   5-10%, it is  understood that the
amplitude  cannot be  measured  with a  better accuracy  than two  significant
figures.

C.5	Associated Period

The period of the  maximum amplitude is measured on  the vertical component at
zero crossings or between two neighbouring peaks or troughs.  Period should be
read to two significant figures and to a maximum precision of 0.01 seconds.

C.6	Back azimuth, apparent angle of incidence, level of
	rectilinearity of the polarized wave.

Back azimuth and angle of incidence  should be computed to  one degree.  Level
of rectilinearity should be computed to 0.01.
	Rectilinearity =1- (a2 + a3)/2a1, 
where a1, a2, a3 are the principle axes lengths of the polarization ellipsoid.

C.7	Secondary Phases

The  standard  notation for  all phases  is  that  used  by the  International
Seismological  Center.  Arrival  times of  clear  identified phases  should be
reported.  Measurements    of   arrival  time,   maximum  recorded  amplitude,
corresponding period, back  azimuths, apparent angles  of incidence and levels
of rectilinearity of secondary phases (when appropriate) follow the same rules
mentioned under 1-6.  It is important that secondary phases, in particular pP,
sP, and PcP are  reported when possible.   Another secondary phase  of special
important for stations at  island or coastal  locations is  the hydro-acoustic
wave  (T-phase).   The reporting  of T-phases  is  recommended to  improve the
network capability in oceanic areas of the southern hemisphere.

C.8	Arrival Time of a Maximum Rayleigh Wave

The arrival time of the maximum trace amplitude  of the Rayleigh wave train is
measured with a precision of 1 second.

C.9	Maximum Amplitude of the Rayleigh Wave

The magnitude  of  the maximum deflection  (center-to-peak from median) of the
Rayleigh wave is measured from  the maximum  trace  amplitude on the  vertical
component, corrected to true  ground motion using the  measured period and the
instrument response curve.   The ground amplitude is reported  in  micrometers
with a maximum precision of 0.001 micrometer.

C.10	Period of the Rayleigh Wave

The observed period of the maximum amplitude  of the Rayleigh wave is reported
in seconds.

C.11	Back azimuth, level of rectilinearity of the Rayleigh wave.

Back   azimuth   is  reported   with  precision  of    one  degree.  Level  of
rectilinearity of the polarised  wave  is reported  with precision of 0.01 for
estimate of the quality of the measurement.

C.12	Noise Amplitude

If no Rayleigh  wave can be  associated  to a detected  P-phase,  the  largest
amplitude of the seismic noise  with period between 10-30  seconds is measured
on the vertical component  within  one minute  of  the section  of the  record
preceding   the initial   P-wave.  The ground    amplitude  in  micrometers is
reported.

C.13	Noise Period

The period of the corresponding noise amplitude is  reported to a precision of
one second.

Practically the same information is  also reported from seismic  arrays.   The
only difference is that, instead of angle of incidence,  the arrays report the
slowness value  dt/d  (s/deg) with a precision  to 0.1, as well as approximate
values for the source parameters (source time, epicentre, mb and Ms).

C.14	Qualitative Remarks

It is very   important  that  the report is  accompanied  by  remarks of   the
experienced  analyst qualifying,  if possible, the character of   the event as
seen from the visual  inspection of  the record or   by  a more  sophisticated
analysis.  The following identifiers are suggested:

CL .. Instrument offscale; accompanied by 999999 on reported
      amplitude.

DD .. Multiple (double) event: complex wave pattern particularly in
      the P-wave group justifying such statement according to the analyst's
      experience.

DE .. Deeper than normal, intermediate; qualification made by the
      analyst if the wave pattern and amplitude ratios of main phases
      warrant it.

LA .. Local event within a very short distance, not possible to
      separate P and S phases.

LB .. Local event within a short distance.  P and S separated but S-P
      interval less than 25 sec. i.e., focal distance less than about
      2 degrees.

ME .. Mixed events: two events overlapping and causing some confusion
      in reading an interpretation: if possible, they should be
      identified (local, regional, teleseismic).

NO .. Non-seismic origin: intended for local disturbances such as
      sonic booms, meteoroids, passing aircraft, etc., which do not
      justify separate codes.  Intended for automatic use in EIDC
      processing, and should generally be accompanied by a separate
      explanation in (( )).

NP .. Confirmation that no corresponding P wave is being reported for
      this event.

PQ .. Possible quarry blast.

QB .. Quarry blast: event announced by responsible authorities as a
      quarry blast, total charge in tons and coordinates should be
      indicated if known.

R ..  Regional event somewhere between 2 degrees and 20 degrees, i.e.,
      the wave pattern is influenced by waves travelling between the crust
      and the 20 degree discontinuity.

RB .. Rock burst: event announced by authorities or qualified to this
      category by a typical wave pattern.

TA .. Teleseismic event, a simple seismogram with largest amplitudes
      within first few seconds.

TB .. Teleseismic event, seismogram is made up of more than one
      discrete arrival.

TC .. Teleseismic event with a complex waveform made up of many
      arrivals.

TU .. Uncertain time: if the time correction is uncertain by more than
      0.05 seconds because of clock problems.

The above parameters  are  transmitted within double  parentheses according to
the  International  Telegraphic  Seismic   Code.  In the  same  way,  location
information (if available) and additional comments may be transmitted.

C.15	NDC Location Information

NDCs are encouraged to provide information on location and other parameters of
seismic events detected at  their  participating stations by  use of a "FOCUS"
group  in their parameter  reports.  Sufficient   information may be available
within  sufficient time from a  local network to  provide this information.  A
"FOCUS" group may also be produced from information recorded at a single array
or three-component station which  has  one defining measurement   of a P  type
phase (i.e., defining observations of time of arrival, azimuth and slowness or
angle of incidence) and one observation of an S-type  phase, provided that the
event is located within 10 degs.  of the station.

If  EIDCs do   not receive  sufficient  additional data  on these NDC-reported
events to undertake a separate  estimate of  the event  parameters,  the  NDC-
reported events will be listed in a separate section  of the unassociated data
in the FEB (see Appendix D, Section D.3.4.2, and Appendix J, Section J.3).

C.16	Abbreviated Reporting

For   practical reasons  of  handling   a  manageable  amount of   data events
classified by the station analyst as

(i)	local earthquakes, quarry blasts or rockbursts
(ii)	belonging to an earthquake sequence (e.g. more than ten events
        a day from the same place)

an abbreviated report would be allowable.

Parameter reports on  local  events should  be limited  to  the  arrival time,
amplitude and period of P, or first clear phase, (parameters 2,  4, 5 of Table
C.1) and a comment on the event.

During an especially large local earthquake sequence, it would be allowable to
give  a general description  of the seismic field,  such  as "A local sequence
took place between (time A) and (time B)", reporting level 1 data only for the
largest event each day, and giving the number of events on that day.

Table C.1
       	   	  	  	  	Unit		Precision of
       	   	  	  	  	of	
Group(1)    Component     Parameter	Measurement	Measurement   Code(2)
-----------------------------------------------------------------------------
IFASE	 Short-period  1. First Arrival
	 vertical	
		       2. Arrival Time	   h, min,s	0.1 s		P

		       3. Time of Maximum
			  Amplitude	   h, min,s	0.1 s		XA

		       4. Amplitude(3) A   nm		as needed(5)	A

		       5. Period T 
	   	  	  corresponding to
		  	  Amplitude A	   s		as needed(5)	T

(COMP3   Short-period  6. Back Azimuth	   degree	1 degree	AZ
/SLOW)	 vertical and
	 horizontal
		       7. Angle of 
		  	  incidence	   degree	1 degree	INC(4)

	(for arrays:	  Slowness	   sec/degree	0.1		SLO)

		       8. Level of
		  	  rectilinearity   ratio	0.01		REC(4)
		  	  (P-only)

(SFASE(n))(6)	       9. Secondary phase
		  	  description:
		  	  Arrival time	   min,s	0.1 s
		  	  Amplitude	   nm		as needed(5)
		  	  Period	   s		as needed(5)
		  	  Back Azimuth	   degree	1 degree
		  	Angle of Incidence degree	1 degree

LPREP(7) Long-period  10. Arrival time of  h, min,s	1 s	      LPZ LR XA
	 vertical	  maximum in the
		  	  Rayleigh wave

		      11. Maximum	   micrometer	as needed(5)	A
		  	  amplitude in the
		  	  Rayleigh wave

		      12. Period of	   s		1 s		T
		  	  corresponding
		  	  Rayleigh wave

	Long-period   13. Back azimuth	   degree	1 degree	AZ
	vertical and
	horizontal

	Long-period	Noise identifier				LPZ NB
	vertical
			
			
		      14. Noise	  	   micrometer	as needed(5)	A
		  	  amplitude

		      15. Noise period	   s		1 s		T
						
(EVCOMM)	      16. Qualitative remarks on
		  	  local and regional events
		  	  (may include locations and
		  	  magnitudes)

_______________________________

1 GROUP names in accordance with Annex D1 of Appendix D.  Parameters
  of GROUPS without parentheses, e.g., IFASE, are mandatory.
  Parameters of GROUPS designated by parentheses (e.g., COMP3) are
  optional.
2 Codes used by the International Seismological Center (ISC) are
  recommended.
3 The value of A corresponds to the maximum amplitude in the interval
  of 0 - 6 seconds after the arrival of the P-wave.  In case of large
  teleseismic events this interval would be extended to 20 seconds.
4 These symbolic designators and the corresponding values are not part
  of the International Seismic Code and must be enclosed in double
  parenthesis (( )).
5 To at least two significant figures, and to a maximum precision of
  0.01 nm or 0.01 seconds.
6 Clear secondary phases should be reported whenever possible.
7 Arrival time, amplitude and period are mandatory for reported
  Rayleigh waves.  Noise identifier, noise amplitude and period are
  mandatory if no Rayleigh wave is reported.


EIDC PROCEDURES FOR PREPARING AND COMPILING THE IEL
(Excerpt from Appendix B, CRP 190/Rev 4, 1990)
 
This appendix describes the procedures for  preparation and compilation of the
Initial Event List  (IEL).  The IEL is  based  on  automatic processing of the
station parameter data directly as reported by the NDC's.
 
Procedures  for  the processing  of  parameter data  were first  described  in
CCD/558 and then further in  CD/43  and  CD/448.  The last  of these gives the
more complete description, in Appendix 7 of Addendum 1 to CD/448 under section
3, entitled "Procedures   for  Automatic Association  and Location of  Seismic
Events", and thus  is the obvious  starting point for any  revised procedures.
The procedures given there  are a combination  of formal rules and suggestions
as to how the bulletin satisfying these rules  might be best achieved.   These
suggestions can be termed "algorithmic" in  nature  and are not mandatory.  As
long as the  IEL contains  only events  which satisfy   rigid event  formation
criteria, the exact means by which these were  produced from the input data is
not of great importance.   The following, derived from Appendix  7 (section 3)
of  CD/448 are  intended as procedures  for GSETT-2.  To facilitate comparison
with the original text, the same headings are kept as far as possible.
 
The objectives of the processing of parameter  data  at EIDCs remain unchanged
from  those described in CD/43:  "The association of  arrival  times should be
carried out in a way that maximizes the probability of defining new events."
 
B.1	Definitions 
 
The process of forming seismic  events and estimating  their origin times  and
hypocenters is here referred to as association and  location.  This process is
based on phases with related phase-names and  observations  reported  from the
seismic stations.
 
A phase refers to  a more or  less prominent onset on the  seismic record that
can be associated with a seismic wave type along some specifiable path through
the earth's interior or along its surface.  Phases  believed to originate from
the same  seismic event are grouped  together with the  first   arriving phase
referred to as the primary  phase and  later phases  referred to as  secondary
phases respectively (Appendix D, Annex D.1, page D39).
 
A phase is described by  a  phase-name (indicating wave  type  and  path).   A
reported phase-name may be changed in the association and location process and
the phase-name  that  is finally  given  by this   process is called  assigned
phase-name.
 
A phase  is  also described   by  one or   more observations.  The   following
observations  can be used in the  association and location  process:  time  of
arrival, back-azimuth, and   slowness  or equivalent  from angle  of incidence
reported by three component station.  Observations of angle  of incidence from
a  three  component   station are initially  converted  to    slowness  in the
association   and location process  using   the  appropriate   (P or S)  phase
velocity.  The appropriate  phase velocity  may have been  provided by the NDC
responsible for the station; in the absence of such information the velocities
of the upper crust (P=5.57  km/s, S=3.37 km/s)  implied in the Jeffreys-Bullen
tables are to be used.
 
A set of joint observations of time of arrival, back-azimuth, and slowness (or
equivalent from  angle of incidence) of a  phase  at an array (or  3 component
station) is called a phase measurement.  That  is to  say a phase measurement,
as defined here, consists of three observations.
  
Phases with related phase-names  and observations underlying the formation  of
seismic events and  the estimation of  origin time and  hypocenter  are called
defining.  A defining  phase  has to  have a defining   time  of  arrival.   A
defining station  has  one or  more defining  phases.   Only certain  types of
phases  may be  used in  this  process.  There are  also  restrictions on  how
reported phase-names may be changed in the association  and  location process.
Furthermore,  a  minimum number  of a certain  combination  of observations is
necessary to form a seismic event. The observations must also  satisfy certain
residual requirements.   The   minimum number of   combinations, the rules for
changing phase-names, and the  residual requirements together define the event
formation criteria.
 
Phases may also be flagged so that they may not be used  as defining for other
events. Phases may also be associated so that they appear in the event listing
even if they are neither defining nor flagged.

B.2	Defining Phase Types 
 
Reported phases  with  the  following  assigned phase-names may  be   used for
forming events:
 
	-	P 
 
	-	PKP (initial DF branch only) 
 
	-	S 
 
	-	local and regional P phases: Pg, P*, Pn 
 
	-	local and regional S phases: Sg(Lg), S*, Sn 
 
	-	depth phases pP, sP 
 
 
A secondary phase may be  defining only if  the corresponding primary phase is
defining.
 
B.3	Event Formation Criteria 
 
Each seismic event in the IEL should meet the following criteria: 

B.3.1	Minimum Number of Observations
 
The formation of  a seismic event  must  be based on defining  phases with  at
least the following minimum numbers of observations or measurements:
 
	(i)Four defining observations, not all of which are related to
	   PKP phases, at three or more stations.
 
OR 
 
	(ii)One defining measurement (i.e., defining observations of
	    time of arrival, azimuth and slowness or equivalent from
	    angle of incidence) at one station and two observations at
	    another station, where at least one of these stations is
	    an array or within 10 degrees of the event.
 
B.3.2	Restrictions on the Use of Reported Phases 
 
The  following restrictions apply to phase-names  assigned  to phases that are
defining:
 
	(i)Phases assigned as P and PKP must have been reported as
	   primary phases

	(ii)Observations of phases reported as originating from local
	    or regional events may be used only within local and/or
	    regional distances (based on qualitative remarks, S-P
	    time, reported location or distance, or phase name, etc.)
 
	(iii)Observations of secondary phases assigned as pP and sP
	     may be used only if reported phase-names were pP, sP, PP,
	     PcP, or unknown.
 
B.3.3	Residual Requirements
 
All observations must have final residuals of less than  1.5 a priori standard
deviations.    These  a priori   standard  deviations  expressed  in  terms of
residuals with respect to the Jeffreys-Bullen travel time table (used  for all
phases in the event location procedure), are as follows:
 
	(i)time of arrival: 
 
			-P (25<distance<100 deg)	1.0 second 
 
			-P (all types;distance<25 deg)	3.0 seconds 
 
			-S (all types)			5.0 seconds 
 
			-PKP (DF branch only)		1.5 seconds 
 
			-pP, sP				2.0 seconds 
 
	(ii)array slowness vector residual (in units of
	    seconds/degree), or equivalent from three component
	    processing:

		          Station/Phase Type 
              _____________________________________________

		  3-Component	 HF Array	 SP Array
	Distance	P-type  S-type	All Phases   All Phases
     ________________________________________________________________

	Local/Regional	4.0	6.0	  2.0		3.0
	(0 - 20 deg) 
	 
	Teleseismic	3.0 	6.0	  2.0		1.5	
	(20 - 105 deg) 
 
	Core		4.0	6.0	  3.0		2.0
     ________________________________________________________________


The slowness vector referred to above has components Sx = S * cos(Az) and Sy =
S * sin(Az) where S is the  scalar slowness and Az the  azimuth.  The slowness
vector residual is the length (scalar) value of the vector  difference between
the observed slowness  vector and that  predicted for the  associated phase by
Jeffreys-Bullen travel time derivative.
 
For SP arrays, the allowable slowness vector residual should decrease linearly
from 3.0 to 1.5 sec/deg over the distance range 17.5 to 22.5 degrees.

B.4	Hypocenter Location 
 
Jeffreys-Bullens travel time tables should be used in the estimation of origin
times and hypocenters of the events.  Only those  observations (time, azimuth,
slowness/incidence angle) classified as defining may be used to locate. If the
arrival time observation  for a  phase is defining,  but  the slowness/azimuth
vector is not, then the arrival  time should be  used to  locate.  However, if
the slowness/azimuth  vector is defining, but the  arrival time  is  not, then
none of the observations should be used.  When the slowness/azimuth vector and
arrival time  are both   defining,  the arrival  time, slowness   and  azimuth
observations  must  all   be used to    locate.  The uncertainties  of  source
parameters  should be  estimated     from the   a priori  standard  deviation.
Uncertainties must be at the  one standard deviation level for  each parameter
(latitude, longitude,  depth,  origin  time).  The    units for  latitude  and
longitude are great circle degrees, for depth are kilometers, and for time are
seconds.

B.5	Flagging of Phases as Removed from Further Consideration 
 
One  way of  avoiding   excessive  processing time would    be to flag  phases
corresponding to events  with five or  more defining  observations at  four or
more stations such  that they may not be  used as defining  for  other events,
provided that they satisfy the following requirements:
 
	(i)The predicted 87% confidence interval of the expected
	   arrival time for the given station and phase should be less
	   than 30 seconds.

	(ii)The arrival time residual should lie in the interval (-3
	    to +10 seconds) or in the smaller of (-c to + 2 c ) and
	    (-5 to +10 seconds) where:
 
		          c**2 = {event, phase}**2 + {phase}**2
 

	{phase}**2 is the a priori standard deviation in the arrival
	time for that phase (section B.3.3), and {event, phase}**2 is
	the standard deviation in arrival time observation predicted
	from the calculated uncertainty in the event location and
	origin time.
 
Non-defining secondary phases (i.e., phases of types other than those given in
section  B.3.3 above) may  also  be flagged,  provided that  they satisfy  the
requirements given above.
 
The following secondary phases should be  flagged for all  events, if assigned
as such:
 
	PKP(BC branch) 
	PKP(AB branch) 
	PP 
 
For large events, with more that 10 defining phases  at distances greater than
25 degrees, the following associated  secondary phases should also be flagged,
subject to the same restrictions, however they may have been reported:
 
	PcP 
	PKKP 
	PKPPKP 	(all branches) 
	SKP 	(all branches) 
 
The a  priori standard deviations of the  arrival times  of these later phases
are:
 
	PcP, PP		2.0 seconds 
	PKP (AB, BC)	1.5 seconds 
	All others	3.0 seconds 
 
B.6	Association of Phases 
 
Phases may be associated to an event so that they  appear in the event listing
even  if they are neither  defining  nor flagged   according to the conditions
given above.  A phase is associated provided at least  one of the following is
true:
 
	(i) the phase arrival time residual lies in the range -5 to
	    +10 seconds
 
OR 
 
	(ii)the phase belongs to the same NDC-reported event section
	    (annex D1, section D1.2.3) as at least one other phase
	    that has been associated, except in cases where the
	    automatic association process has determined that the
	    phase is defining for another event.

Note that phases may be multiply associated if they are not flagged.  However,
associated but unflagged  arrivals  may later become defining, whereas flagged
phases may not.
 
Note that  defining phases for a  given event need  not necessarily be flagged
for that event, and in such  a case are "free" to  become  defining to a later
event.  If they are  also flagged by a  later   event,  they may no longer  be
defining phases for  the earlier event  and  this  may  then  require that the
earlier event   be deleted  if  the event  formation criteria are   no  longer
satisfied.  If a given phase appears to be defining  to both  (a contradiction
in terms), but is flagged for neither, both events have to  be included in the
IEL.
 
B.7	Amplitude Consistency Check 
 
CD/43 recommends the application of statistical  procedures involving not only
the stations which have defining  phases but also those  which have not.  This
information is compared with a priori estimates  of detection  capabilities of
the individual stations for an event, in order to establish whether or not the
pattern of stations  with   and  without defining   phases  fulfills a  preset
probability requirement for forming an event.
 
Potentially this method  is very  powerful in  deciding  whether or not  small
events, which only just satisfy event  formation criteria, are valid, and this
technique should routinely be applied only to events with defining phases from
six stations or less.  It can  be  used  to  point  out inconsistencies in the
solution without affecting the solution, for larger events.
 
B.8	Calculation of Body Wave Magnitude 
 
Individual station body wave magnitudes should be computed using the amplitude
and  period observations, corrected    for distance by  the  Gutenberg-Richter
amplitude-distance  relation.  Station  magnitudes should only  be  calculated
from observations for which the corresponding phase is defining for the event,
and only for distances greater than 20 degrees.
 
Event magnitudes  based on  the  average of  individual station magnitudes are
often strongly  biased, and  maximum likelihood methods  should  be applied in
computing them.  Care should be exercised  in the application of such methods,
as the a  priori estimates of  station noise levels and/or detectability often
appear to be over-optimistic.  The average magnitude should also be reported -
in calculating this average observations differing from the mean  by more than
3 standard deviations should be excluded and the mean then recomputed.
 
B.9	Association of Long-Period Data 
 
Reported   long-period data  should   be    associated with an  event  if  the
theoretical arrival  time at  the  reported period   agrees  with the reported
arrival time of the maximum of the Rayleigh wave within three minutes plus one
tenth  of   the  theoretical  travel time.  The  theoretical   travel  time is
calculated  according to the method  given  in Appendix 6.5  of  CD/43.   This
procedure may give rise to multiple associations, which  should be resolved as
follows:
 
	(i)If back-azimuth is reported, it is not allowed to deviate
	   more than 50 degrees from the calculated
	   station-to-epicenter azimuth;
 
	(ii)If the arrival time residual of one of the events is less
	    than three minutes, associations with a time residual of
	    more than five minutes should be excluded;
 
	(iii)Amplitude consistency checks, as described in sub section
	     7 above for short-period data, should be applied.
 
If multiple associations cannot be resolved  by any of the above,  the surface
wave report should not  be allowed to enter into  the calculation  of an event
surface wave magnitude.
 
B.10 Calculation of Surface Wave Magnitude 
 
Individual station magnitudes should  be calculated using  the Prague formula.
Maximum likelihood techniques, as described in sub-section 10 above, should be
used to calculate the event surface wave magnitude.



EIDC PROCEDURES: INSTRUCTIONS FOR PREPARING CELS USING WAVEFORM
       ANALYSIS
(Excerpt from Appendix F, CRP 190/Rev 4, 1990)

The use of global network waveform data for seismic bulletin preparation is in
its infancy.  Strict rules  for the waveform analysis  are therefore difficult
to define at this point in  time and the  procedures  suggested here should be
considered only as preliminary  examples  of what kind of processing  might be
useful preparing the event lists.
 
This appendix describes the preparation and  compilation of the  Current Event
List (CEL).  This process is based on information  initially obtained from all
IELs, analysis  of   waveform data  and seismological  judgement   and, as  it
proceeds, from the  CELs.  The preparation  of CELs will  thus  be a bootstrap
process with each EIDC updating its own CEL to reflect the results of waveform
analysis and seismological judgements  as  they are made in the interpretation
of events.  In turn,  information contained in a  CEL will provide a basis for
various hypotheses which will be tested by the analysis of waveform data.
 
The objectives of  CELs are to  upgrade the quality  of the IEL by  extracting
additional information not normally available or apparent to the NDC analysts,
and to correct existing information.  The preparation of CELs is guided by the
same principle as the  automatic formation of IELs, that  is to  maximize  the
number of valid events.
 
Each EIDC will exchange CELs daily and will be  responsible for  reviewing the
information combined in all other CELs in order to converge on a common set of
results among   the  EIDCs.  This  reconciliation should  minimize differences
prior to merging CELs to form a Final Event Bulletin.
 
F.1	Content of the CEL 
 
Preparation of the CELs includes use of the  IELs of all EIDCs,  the routinely
reported  station parameter  and   waveform data, and    supplemental  station
parameter and waveform data that may be requested in the course of interactive
analysis.
 
The preparation and compilation of the CELs involve daily editions of the CEL.
The last CEL will represent the EIDCs view of  what should appear in the final
event bulletin, the FEB.
 
F.2	Rules 
 
	The information in the  last edition of the  CEL should be unique with
respect to event hypotheses as well as defining phases.
 

	Each event included in   the   list should  meet the   event formation
criteria  of Appendix B  with the exception   that the standard  deviation may
exceed the  rules by 20% provided   that additional confirmatory seismological
evidence is available.
 
	All defined events must be seismologically sound. 
 
	Phases reported by the NDCs, or new  phases defined by the  IDCs, must
be  entered only  once  as   defining in   the bulletin,  or   in the list  of
unassociated phases.  If a phase initially appears as  defining with more than
one  event or with more  than one phase name  for one event  in the  CEL,  the
analyst must select  only  one of the  options  using his  best  seismological
judgement.   Comments may be entered  to note any   remaining ambiguity in the
analyst's mind.
 
	All phases belonging to  the  same  event section (annex  D1,  section
D1.2.3) will remain together  in chronological order  in either the associated
or   unassociated event lists,   unless the EIDC determines   that   the phase
originated from another event.
 
	All  changes to information  originally reported by the  NDCs  must be
explained by use of comment codes, as follows:

		N - the reported phase name has been changed.

		M - one or several of the parameters reported by the
		    NDC for this phase has been remeasured by the
		    EIDC.
 
		D - phases reported by the NDC as being from the same
		    event have been disassociated by the EIDC.

		A - phase added by the EIDC.

		The comment codes can be combined.

F.3	Analysis Procedures and Guidelines 
 
The analysis steps suggested for  preparation of CELs  are grouped together in
five categories that largely make up one cycle in the analysis:
 
	(i)	determine data to be requested; 

	(ii)	reject spurious event hypotheses; 
 
	(iii)	improve event solutions; 
 
	(iv)	form additional events; 
 
	(v)	review unassociated phases; 
 
It may be necessary to iterate through this cycle several times.
 
F.3.1	Determine data to be requested 
 
On the basis of the EIDC event lists and  the available station  parameter and
waveform data, supplemental data that need to be requested for  the subsequent
analysis are determined and are requested.
 
F.3.2	Reject Spurious Event Hypotheses
 
The automatic  location and association  for the  IEL often generates spurious
events that can be rejected by waveform analysis and seismological judgements.
 
Events formed by Multiple Phase Associations 
 
Events  generated  by the  automatic IEL procedures   may contain observations
which are multiply defining.   The result  of the analysis should  be that the
EIDC must determine from which of the events the phase originated.   Once this
determination is made, the  phase in question must  be removed  from all other
event hypotheses  and  this may require that some   other event hypothesis  be
rejected.
 
Split Events 
 
The large number of phases that are generated by a large seismic event may not
all be associated  with  the  event in the  automatic association and location
process that results in the IEL.  Quite often such  unassociated phases become
"free" and  generate spurious so called  split events,  which  frequently have
origin times and  hypocenters close  to those of  the large event.   The EIDCs
should determine when this has happened and reject the split event.
 
Other spurious Events 
 
Because  of the  large number of  phases reported  from  the  station network,
events  may sometimes be generated  in the automatic  association and location
process from phases that by chance  meet the  event formation criteria.  EIDCs
should use waveform analysis to assist with the  identification of such events
and reject them.
 
F.3.3	Improve Event Solutions 
 
Many of the events that are located in the automatic  processing are small and
are often afflicted with large  estimated  errors in hypocentral co-ordinates,
in particular depth.    There   are  a  large  number of  analysis  steps  and
processing techniques that  should be applied   to improve the quality of  the
event location:
 
	Disassociate and Reassociate Phases 
 
	Select Among Multiply Associated Phases.   

The EIDCS should try to develop automated procedures  to correctly associate a
phase to one event only.
 
	Verify and Improve Reported Parameter Measurements 
 
	Rename Phases 
 
	Add Phases 
 
	Search for and identify depth phases to assist in event
        definition.
 
	Search for and identify secondary phases, e.g. PP and PcP,
        which could help confirm an event solution.
 
	Resolve possible Interference of Surface Waves 
 
	Characterize arrivals by correlation with data from reference
        events.
 
F.3.4	Form Additional Events 
 
Many events are reported by NDCs but are not included in the  IELs.  These NDC
event   hypotheses are obvious starting  points  in the search  for additional
events and waveform analysis would aim at associating additional observations.
 
Phases that could be  available to generate  additional events may be obtained
from  phases  of events  that  are rejected (see  Section  F.3.2  above), from
additional phases added by EIDCs and from the review of unassociated phases.
 
F.3.5	Review Unassociated Phases
 
The analysis of unassociated arrivals should aim at characterizing the signals
so  that  as much as  possible  can   be said about their origin,   even if no
hypocenter estimate can be obtained.

F.4	Required Analysis Techniques 
 
The   EIDCs should be  able to  display  waveforms and perform standard signal
processing (bandpass  filtering,   deconvolution,   and    cross-correlation).
Information  regarding  reported  or  expected   secondary  phases should   be
available.   The EIDCs should  also be able to  repeat the waveform processing
done at the NDCs.
 
EIDC PROCEDURES: COMPILATION OF THE FINAL EVENT BULLETIN 
(Excerpt from Appendix J, CRP 190/Rev 4, 1990)
 
This appendix  describes the  procedures  for  compilation of the  Final Event
Bulletin (FEB). The FEB is compiled automatically from the final CELs reported
by  all four of the EIDCs.   The final  CELs are  merged  so that identical or
similar event solutions are represented only once in the FEB, which  thus will
contain a list of "unique"  seismic events.  Supporting station parameter data
are also listed for each such "unique" event.
 
J.1	Definitions 
 
An event group contains all event solutions from the final CELs whose location
and origin time are  within 3  degrees and 60 seconds,  respectively,  of  the
location and origin time of one other event in the group. Also, if there is an
event that does not meet  the distance and  time requirements but that has two
or more defining phases in common  with another event, then  this event should
be put into a common event group, unless the originating EIDC insists  that it
be reported separately.
 
A representative  event  is the event solution  chosen  to represent  an event
group in the FEB.

J.2	Criterion for Choosing Representative Event 
 
One EIDC solution  is  chosen to be  representative of each event group.    If
there are five or more defining observations:
 
	the representative solution is the one with the maximum number
	of defining observations.
 
	if two or more solutions have an equal number of defining
	observations, the next selection criterion is the solution
	with the maximum number of defining time observations.

	if two or more solutions have an equal number of defining time
	observations, the next selection criteria is the solution with
	the smallest sum of the squares of the residuals for the
	defining time observations.
 
If there are fewer than five defining observations: 
 
	the representative solution is the one which contains the
	defining observation with the smallest station-to-event
	distance.
 
The event parameters for the representative solution are presented in the FEB.
In addition event parameters are given  for non-representative solutions of an
event  group, if any, as comments  (see example) following the presentation of
the event    parameters of the  representative solution.    A   maximum of one
additional comment line must  be presented for each  EIDC CEL  solution  if it
exists.
 
All phases and only those phases associated with  the representative event are
listed with the event.
 
J.3	Listing of Unassociated Phases 
 
The list of unassociated phases should include all phases that  are not listed
as defining or associated with an event.  If a phase is within 3  seconds of a
retimed phase from the same station  that is associated  with a representative
event, then the phase is considered  to be the same  as the associated one and
thus is excluded from the unassociated phase  list.  The unassociated data are
listed in two sections.  The first section contains locations provided by NDCs
via  a  FOCUS line,  together   with their corresponding  phases.  The  second
section contains  all  other  unassociated  data.  (See Appendix   D,  Section
D.3.4.2.)

J.4	Format for an Abbreviated Final Event Bulletin 
 
A message format to be used for an abbreviated final event bulletin is defined
here.
 
This  message  contains only seismic   event  source  parameters (origin time,
hypocenters, magnitudes  etc.)  and no  lists of  associated and  unassociated
station parameter reports.
 
All EIDC  events are grouped  together  according to  the procedures   for the
complete final event bulletin.
 
This abbreviated  FEB  would provide  participants, in  summary  form, with  a
complete list  of all  seismic  events  reported by  the   EIDCs in one  short
message.
 
It would  also  serve to  provide  a  convenient  overview of differences  and
similarities in EIDC seismic event solutions.
 
J.4.1	Header Identification 
 
This message uses the header identification XB02 in the message header.
 
J.4.2	Structure of Data Section 
 
The data section of the message consists of a listing of event groups.
 
J.4.3	Format 
 
The format of the abbreviated bulletin will be identical to the event sections
(Appendix D, Section D.3.4.1) of the FEB.