REPORT FOR THE ACTIVE SEISMIC DATA ACQUIRED IN THE 2003 POTRILLO VOLCANIC FIELD (PVF) SEISMIC INVESTIGATION, SOUTHERN NEW MEXICO AND EL PASO, TEXAS REGION

by Matthew G. Averill1, Kate C. Miller1, Steven H. Harder1,

2003

# 1Dept. of Geol. Sci., Univ. Texas at El Paso, TX 79968

# Abstract

This report describes the acquisition, processing, and quality of the wide-angle reflection and refraction seismic data obtained in the Potrillo Volcanic Field (PVF) seismic investigation of the Southern Rio Grande Rift performed in May of 2003.  This experiment recorded an approximately 205 km long, east-west trending, single channel, wide-angle reflection and refraction seismic profile in southern New Mexico and far west Texas.  Data was acquired using 793 seismographs and 9 shot points utilizing approximately one ton charges.  Station spacings along the profile were designed to acquire wide-angle reflection data across the Potrillo Volcanic Field located in the central portion of the profile as well as to determine basin geometry within Ft. Bliss military base on the eastern end of the profile.  Therefore 509 seismographs were deployed at nominal 100 meter spacing across the volcanic field, 58 seismographs were deployed at nominal 200 meter spacing within Ft. Bliss on the eastern end of the profile and the remaining 226 instruments were deployed at nominal 600 meter spacing.  Shot points were located at each end of the profile, at each end of the central wide-angle deployment with one in the middle, on the western end of the military base used for reversal of the east end shot point and bisecting the west end deployment.

The broad goal of the entire profile is to investigate the structural and seismic velocity characteristics of the Southern Rio Grande Rift (SRGR) and the associated Potrillo Volcanic Field.  The wide-angle deployment across the volcanic field was designed to observe the structural layering underlying this region of the SRGR and will be used in unison with current xenolith studies from local maars.  In this report, we provide information as to the design of the experiment, the data acquisition, processing and merging of the data, and the preliminary quality of the acquired profiles.  We also describe the format and content of the archival tapes containing the SEGY formatted, common shot gathers.  Preliminary data observations show pronounced reflections underlying the Potrillo Volcanic Field region with exceptional signal coverage along the entire length of the profile for all, but one shot (shotpoint 9).

# INTRODUCTION

In May of 2003 the PVF (Potrillo Volcanic Field) seismic survey was performed to investigate the crustal structure across the southern Rio Grande Rift and the PVF in Southern New Mexico and Far West Texas.  This experiment utilized approximately 800 seismic recording instruments, called Texans, provided by the University of Texas at El Paso and the PASSCAL instrument center in Socorro New Mexico as well as volunteers from 6 universities within the US and the United Kingdom.  The purpose of PVF was to obtain two-dimensional structural control across the Potrillo Volcanic Field and a portion of the southern Rio Grande Rift in order to better understand crustal evolution through magmatism due to extension.

In this report we describe the data collected in the May 2003 PVF experiment.  We will provide information pertaining to the data acquisition and formatting for this experiment, which included 9 shots along a 205 km long profile using 793 instruments.

# DATA ACQUISITION

# Experiment Design

The Potrillo Volcanic Field (PVF) seismic investigation was designed to acquire wide-angle reflection as well as refraction coverage along an east-west profile across the Southern Rio Grande Rift (SRGR) in southern New Mexico and far west Texas.  The location and length of this 205 km long profile was determined by factors including: 1) Desired geologic targets such as the PVF and the SRGR; 2) Available seismic instruments; 3)  Deployment logistics across southern New Mexico, the city of El Paso and Ft. Bliss Military base.  Utilization of New Mexico highway 9 (Columbus Hwy) across southern New Mexico provided the truest East-West profile and easiest deployment logistics for this study.  The hwy was used to deploy portions of the profile west of Columbus, NM and from approximately 15 miles east of Columbus, NM to the eastern edge of the West Mesa near Santa Teresa, NM.  The western most section of the profile involved the usage of private farmland roads, Bureau of Land Management 4WD access roads and one 9 mile hiking section.  Deployment across the city of El Paso and into Ft. Bliss Military base required permissions from private residences, placement on public properties and special permissions from Ft. Bliss.  The profile was broken into four sections with a change in station spacing for each section.  Closer station spacing was used to acquire wide-angle reflection data across the PVF and within Ft. Bliss military base at the eastern end of the line.

Station and shotpoint numbers increase from west to east along the profile (Figure 1).  Station 1001 and shotpoints 1 and 2 are located approximately 30 miles S. of Hacita, NM in the valley west of hwy.  Stations 1002-1153 are located at 600 m eastward relative offset from the west end to the east end of Columbus valley approximately 20 miles east of Columbus, NM.  Station 1154 begins 100 m station spacing from the eastern edge of the Columbus valley and continues eastward to station 1663 approximately 50 km east along the highway.  Within this 100m section there are two sections of 200 m spacing from stations 1256 to 1271 and 1519 to 1534 used to maximize the use of the available instruments.  Stations 1664 through 1693 are located at 600 m spacing along the highway eastward to the edge of the mesa.  Stations from the mesa across El Paso, the Franklin Mountains and down into Ft. Bliss (1694-1737) are at 600 m spacing.  Starting at station 1737 approximately 1.5 km west of loop 375 inside Ft. Bliss, stations 1737 through the east end at station 1795 and shotpoints 8 and 9 are located at 200 m spacings.

# Seismographs

Instrumentation used for this experiment solely consisted of “Texans” provided by UTEP and PASSCAL.  The Texans are single-component digital seismographs that record the signal from a single Mark Products® 1-10B vertical-component 4.5-Hz. Geophone.  Using these instruments we enjoyed an approximate 99% data recovery.

# Seismograph Deployment

Of the 793 Texan seismographs deployed, 72 were deployed on May 9th while the remaining 721 instruments were deployed on May 10th.  All the instruments were picked up on May 11th.  One instrument was missing upon retrieval, but was located on the 12th.

# Shotpoints

Shot holes were drilled and loaded between the dates of April 22 and May 17.  The shots were detonated on the morning of May 18 between 12:00 AM and 4:00 AM Mountains standard time.

A total of 9 shots were recorded from 9 shotpoints numbered from west to east 1 through 9 (Figure 1).  Two shots were recorded at both the west (1 and 2) and east (8 and 9) ends of the profile to allow stacking.  Shot 3 was located approximately 100 m North of the Mexico border, 15 km West of Columbus, NM, just East of the Carzalia Onion farm property.  Shots 4 and 6 were located on the West and East side of the 100 m wide-angle deployment on the eastern edge of the Columbus valley and 100m North of highway just west of mile marker 140.  Shot 5 was centrally located within the wide-angle deployment approximately 100 m North of the Mexico border, 1 km South and 1 km East of mile marker 117.  Shot 7 was located within Biggs approximately 1 km West of loop 375 and will be used for reversal of shots 8 and 9.  Shots 1,4,6,7,8 were loaded with 2000 lbs (909.1kg) of Slurran 406, shots 2 and 9 were loaded with 2500 lbs (1136.4 kg) of emulsion, shot 3 was loaded with 1200 lbs (545.5 kg) of Slurran 406 and shot 5 was loaded with 2800 lbs (1272.7 kg).  The main charge for each shot was detonated using 1 lb boosters ignited by Primacord® detonating cord.  The detonating cord was ignited by an electrical blasting cap using a UTEP designed “seismic initiator” linked to a Reftek 111A GPS clock.  Table 1 provides shotpoint location information from west to east.  Shot point latitude and longitudes are given in NAD 27 datum for UTM zone 12 and 13 northings and eastings.

# Data Downloading

Data recorded by the Texans were downloaded on the day of retrieval.

# Station and Shotpoint Locations

Shotpoint and seismograph locations and elevations are provided in Tables 1 and 2 and are based on differential GPS measurements, using the North American 1927 Datum (NAD 27) and are presented in UTM zone 12 and 13 eastings and northings.  The GPS receiver occupied each station location for no less than 15 seconds, yielding a nominal horizontal spatial accuracy of about 0.5 m and a vertical accuracy of approximately 1 m.

Figure 1.  Location map for the Potrillo Volcanic Field (PVF) experiment.

SEGY DATA MERGING

# Station numbers

Receiver stations were numbered 1001 to 1795 from West to East.  Stations 1156 and 1722 were omitted due to no deployment at that station location.

# UTM coordinates

Station 1001-1057 and shotpoints 1-2 are located in UTM zone 12, while stations 1058-1795 and shotpoints 3-9 are located in UTM zone 13 and is indicated as such in tables 1 and 2.

# Texan data processing

Clock drift correction: previously made during preprocessing of Texan data.

# Debias by subtracting the mean trace amplitude from every sample

Put UTM geometry into SEGY headers

# SEGY Trace Format

SEGY trace header formats are described in Table 3 and are modified from described format of Barry et al. (1975).  The data trace values are written as 32 bit, IBM floating-point numbers (SEGY standard) as ouput from PROMAX.  All nine shot gathers were merged into one SEGY file.  There are 793 total traces per shot gather each with fifty seconds of saved data.

# References:

# TABLE 1:  SHOTPOINT DATA TABLE

| Shotpoint | Latitude | Longitude | Arcsecond Latitude | Arcsecond Longitude | UTM Easting* | UTM Northing* | Elevation |
| --- | --- | --- | --- | --- | --- | --- | --- |
| SP1 | 31.78686 | -108.373 | 114432.6969 | -390143.592 | 748730 | 3519629 | 1328.906 |
| SP2 | 31.7865 | -108.373 | 114431.399 | -390143.6287 | 748730 | 3519589 | 1328.909 |
| SP3 | 31.78436 | -107.767 | 114423.7026 | -387960.4397 | 238001 | 3519681 | 1301.146 |
| SP4 | 31.8265 | -107.394 | 114575.4147 | -386617.5958 | 273436 | 3523515 | 1203.079 |
| SP5 | 31.78376 | -107.148 | 114421.5372 | -385733.9218 | 296580 | 3518290 | 1234.701 |
| SP6 | 31.81021 | -106.819 | 114516.7736 | -384548.8244 | 327805 | 3520654 | 1248.372 |
| SP7 | 31.84681 | -106.341 | 114648.5198 | -382828.9838 | 373081 | 3524053 | 1205.529 |
| SP8 | 31.88744 | -106.217 | 114794.7991 | -382379.8046 | 384938 | 3528418 | 1233.645 |
| SP9 | 31.88771 | -106.217 | 114795.7696 | -382380.1981 | 384928 | 3528448 | 1234.706 |

*  Shotpoints 1 - 2 UTM zone 12

*  Shotpoints 3 - 9 UTM zone 13

# TABLE 2:  RECEIVER DATA TABLE 1

| Station number | Latitude | Longitude | UTM Easting* | UTM Northing* | Elevation (m) | 1028 | 31.81438 | -108.194 | 765666 | 3523106 | 1442.964 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1001 | 31.78666 | -108.373 | 748725 | 3519607 | 1330.658 | 1029 | 31.81737 | -108.187 | 766298 | 3523454 | 1434.906 |
| 1002 | 31.77754 | -108.37 | 749076 | 3518604 | 1332.578 | 1030 | 31.81917 | -108.18 | 766930 | 3523670 | 1427.162 |
| 1003 | 31.76925 | -108.365 | 749547 | 3517695 | 1339.329 | 1031 | 31.82234 | -108.173 | 767578 | 3524039 | 1420.182 |
| 1004 | 31.76758 | -108.358 | 750191 | 3517526 | 1344.967 | 1032 | 31.82295 | -108.167 | 768169 | 3524122 | 1420.997 |
| 1005 | 31.76628 | -108.353 | 750715 | 3517394 | 1349.85 | 1033 | 31.82082 | -108.161 | 768756 | 3523901 | 1413.817 |
| 1006 | 31.76524 | -108.347 | 751289 | 3517292 | 1354.519 | 1034 | 31.81845 | -108.154 | 769371 | 3523654 | 1402.872 |
| 1007 | 31.76366 | -108.341 | 751883 | 3517131 | 1358.534 | 1035 | 31.81649 | -108.149 | 769929 | 3523451 | 1394.818 |
| 1008 | 31.76179 | -108.335 | 752464 | 3516938 | 1365.277 | 1036 | 31.82411 | -108.141 | 770609 | 3524315 | 1389.95 |
| 1009 | 31.76072 | -108.328 | 753040 | 3516833 | 1370.661 | 1037 | 31.84435 | -108.134 | 771189 | 3526576 | 1386.252 |
| 1010 | 31.76213 | -108.322 | 753617 | 3517004 | 1376.388 | 1038 | 31.84644 | -108.126 | 771979 | 3526829 | 1393.227 |
| 1011 | 31.76144 | -108.316 | 754221 | 3516943 | 1379.907 | 1039 | 31.84419 | -108.12 | 772501 | 3526593 | 1391.64 |
| 1012 | 31.76341 | -108.308 | 754936 | 3517179 | 1388.736 | 1040 | 31.84125 | -108.113 | 773187 | 3526285 | 1393.61 |
| 1013 | 31.76639 | -108.301 | 755668 | 3517527 | 1396.711 | 1041 | 31.83899 | -108.108 | 773709 | 3526049 | 1395.375 |
| 1014 | 31.77319 | -108.292 | 756416 | 3518301 | 1405.2 | 1042 | 31.83653 | -108.102 | 774305 | 3525791 | 1395.987 |
| 1015 | 31.77734 | -108.284 | 757175 | 3518780 | 1415.018 | 1043 | 31.83382 | -108.095 | 774898 | 3525506 | 1392.967 |
| 1016 | 31.77881 | -108.278 | 757794 | 3518959 | 1419.494 | 1044 | 31.83163 | -108.09 | 775461 | 3525278 | 1395.381 |
| 1017 | 31.77931 | -108.271 | 758405 | 3519030 | 1422.516 | 1045 | 31.82889 | -108.083 | 776098 | 3524991 | 1395.956 |
| 1018 | 31.77952 | -108.265 | 759029 | 3519069 | 1426.397 | 1046 | 31.82648 | -108.077 | 776670 | 3524739 | 1394.351 |
| 1019 | 31.78063 | -108.258 | 759665 | 3519208 | 1430.856 | 1047 | 31.82409 | -108.071 | 777231 | 3524490 | 1391.136 |
| 1020 | 31.78224 | -108.251 | 760283 | 3519402 | 1435.088 | 1048 | 31.82181 | -108.066 | 777761 | 3524250 | 1387.526 |
| 1021 | 31.78424 | -108.244 | 760937 | 3519640 | 1440.713 | 1049 | 31.81883 | -108.058 | 778471 | 3523938 | 1385.373 |
| 1022 | 31.78681 | -108.237 | 761592 | 3519942 | 1447.298 | 1050 | 31.8166 | -108.053 | 778984 | 3523705 | 1389.183 |
| 1023 | 31.79133 | -108.23 | 762294 | 3520461 | 1456.527 | 1051 | 31.81516 | -108.046 | 779624 | 3523562 | 1392.635 |
| 1024 | 31.79522 | -108.223 | 762971 | 3520911 | 1465.624 | 1052 | 31.81557 | -108.04 | 780174 | 3523623 | 1396.609 |
| 1025 | 31.79864 | -108.216 | 763631 | 3521307 | 1481.476 | 1053 | 31.81641 | -108.033 | 780834 | 3523735 | 1399.125 |
| 1026 | 31.80241 | -108.208 | 764293 | 3521742 | 1478.176 | 1054 | 31.81726 | -108.027 | 781431 | 3523845 | 1394.926 |
| 1027 | 31.80917 | -108.201 | 764987 | 3522510 | 1458.522 | 1055 | 31.81806 | -108.021 | 781999 | 3523950 | 1396.189 |
| 1056 | 31.81893 | -108.014 | 782628 | 3524064 | 1393.21 | 1086 | 31.79184 | -107.824 | 232583 | 3520650 | 1290.477 |
| 1057 | 31.82017 | -108.008 | 783214 | 3524218 | 1394.899 | 1087 | 31.79189 | -107.818 | 233165 | 3520641 | 1292.821 |
| 1058 | 31.82182 | -108.001 | 783920 | 3524420 | 1400.97 | 1088 | 31.79182 | -107.812 | 233753 | 3520618 | 1296.78 |
| 1059 | 31.82256 | -107.993 | 216660 | 3524486 | 1395.192 | 1089 | 31.79202 | -107.805 | 234390 | 3520623 | 1300.368 |
| 1060 | 31.81608 | -107.988 | 217137 | 3523754 | 1387.333 | 1090 | 31.79205 | -107.799 | 234972 | 3520612 | 1304.981 |
| 1061 | 31.81373 | -107.981 | 217769 | 3523475 | 1395.534 | 1091 | 31.7917 | -107.793 | 235576 | 3520557 | 1305.382 |
| 1062 | 31.81393 | -107.975 | 218382 | 3523481 | 1405.439 | 1092 | 31.79204 | -107.786 | 236179 | 3520580 | 1306.881 |
| 1063 | 31.81734 | -107.968 | 219003 | 3523843 | 1413.712 | 1093 | 31.79204 | -107.78 | 236780 | 3520564 | 1307.165 |
| 1064 | 31.8181 | -107.962 | 219633 | 3523909 | 1394.762 | 1094 | 31.79291 | -107.773 | 237412 | 3520645 | 1310.275 |
| 1065 | 31.8177 | -107.956 | 220224 | 3523849 | 1384.339 | 1095 | 31.79575 | -107.767 | 238686 | 3521289 | 1315.326 |
| 1066 | 31.81893 | -107.949 | 220829 | 3523969 | 1377.375 | 1096 | 31.79901 | -107.76 | 239286 | 3521376 | 1320.662 |
| 1067 | 31.82257 | -107.943 | 221448 | 3524356 | 1363.886 | 1097 | 31.79993 | -107.754 | 239925 | 3521351 | 1323.227 |
| 1068 | 31.82187 | -107.936 | 222082 | 3524261 | 1355.715 | 1098 | 31.79985 | -107.747 | 240512 | 3521482 | 1323.954 |
| 1069 | 31.82171 | -107.93 | 222670 | 3524228 | 1349.134 | 1099 | 31.80116 | -107.741 | 241110 | 3521438 | 1327.803 |
| 1070 | 31.82121 | -107.924 | 223260 | 3524157 | 1338.719 | 1100 | 31.80091 | -107.734 | 241746 | 3521537 | 1319.159 |
| 1071 | 31.81911 | -107.917 | 223848 | 3523907 | 1329.981 | 1101 | 31.80194 | -107.728 | 242276 | 3521383 | 1306.621 |
| 1072 | 31.81893 | -107.911 | 224451 | 3523872 | 1320.6 | 1102 | 31.80067 | -107.722 | 242903 | 3521461 | 1301.674 |
| 1073 | 31.8188 | -107.905 | 225049 | 3523841 | 1312.22 | 1103 | 31.80151 | -107.716 | 243507 | 3521616 | 1298.393 |
| 1074 | 31.81631 | -107.899 | 225618 | 3523550 | 1308.194 | 1104 | 31.80305 | -107.709 | 244138 | 3521797 | 1292.248 |
| 1075 | 31.81019 | -107.893 | 226141 | 3522856 | 1300.168 | 1105 | 31.80483 | -107.703 | 244752 | 3521988 | 1287.961 |
| 1076 | 31.79916 | -107.887 | 226678 | 3521618 | 1287 | 1106 | 31.80669 | -107.696 | 245374 | 3522163 | 1283.314 |
| 1077 | 31.79182 | -107.882 | 227114 | 3520791 | 1280.398 | 1107 | 31.8084 | -107.69 | 246046 | 3522401 | 1277.765 |
| 1078 | 31.79164 | -107.875 | 227725 | 3520756 | 1277.51 | 1108 | 31.81069 | -107.683 | 246598 | 3522729 | 1272.559 |
| 1079 | 31.79168 | -107.869 | 228354 | 3520743 | 1275.477 | 1109 | 31.81377 | -107.677 | 247313 | 3523162 | 1266.885 |
| 1080 | 31.79177 | -107.863 | 228905 | 3520738 | 1273.69 | 1110 | 31.81783 | -107.669 | 247978 | 3523408 | 1260.053 |
| 1081 | 31.79182 | -107.856 | 229531 | 3520728 | 1275.519 | 1111 | 31.82019 | -107.662 | 248511 | 3523604 | 1254.638 |
| 1082 | 31.79213 | -107.851 | 230070 | 3520748 | 1280.948 | 1112 | 31.82208 | -107.657 | 249163 | 3523837 | 1251.068 |
| 1083 | 31.79215 | -107.844 | 230679 | 3520734 | 1284.252 | 1113 | 31.82432 | -107.65 | 249729 | 3524015 | 1244.566 |
| 1084 | 31.79209 | -107.838 | 231324 | 3520711 | 1287.136 | 1114 | 31.82605 | -107.644 | 250379 | 3524314 | 1240.791 |
| 1085 | 31.7921 | -107.83 | 232013 | 3520694 | 1287.733 | 1115 | 31.8289 | -107.637 | 250973 | 3524582 | 1236.046 |
| 1116 | 31.83144 | -107.631 | 251656 | 3525030 | 1230.28 | 1146 | 31.82746 | -107.441 | 269575 | 3523700 | 1209.342 |
| 1117 | 31.83563 | -107.624 | 252235 | 3525018 | 1226.836 | 1147 | 31.82739 | -107.435 | 270148 | 3523679 | 1209.704 |
| 1118 | 31.83564 | -107.618 | 252827 | 3524996 | 1224.81 | 1148 | 31.82732 | -107.429 | 270738 | 3523621 | 1209.751 |
| 1119 | 31.83557 | -107.612 | 253395 | 3524995 | 1222.294 | 1149 | 31.82692 | -107.422 | 271387 | 3523586 | 1208.846 |
| 1120 | 31.83569 | -107.606 | 254014 | 3524980 | 1221.514 | 1150 | 31.82674 | -107.415 | 271973 | 3523589 | 1208.739 |
| 1121 | 31.83568 | -107.599 | 254605 | 3524942 | 1220.76 | 1151 | 31.82688 | -107.409 | 272556 | 3523567 | 1207.723 |
| 1122 | 31.83546 | -107.593 | 255235 | 3524942 | 1221.19 | 1152 | 31.82679 | -107.403 | 273170 | 3523534 | 1208.944 |
| 1123 | 31.83561 | -107.586 | 255851 | 3524919 | 1221.29 | 1153 | 31.82663 | -107.397 | 273771 | 3523521 | 1208.747 |
| 1124 | 31.83553 | -107.58 | 256436 | 3524923 | 1221.327 | 1154 | 31.82663 | -107.39 | 273871 | 3523525 | 1231.923 |
| 1125 | 31.83569 | -107.574 | 257034 | 3524908 | 1219.979 | 1155 | 31.82668 | -107.389 | 273974 | 3523520 | 1239.758 |
| 1126 | 31.83568 | -107.567 | 257613 | 3524878 | 1220.135 | 1157 | 31.82653 | -107.387 | 274077 | 3523504 | 1245.473 |
| 1127 | 31.83554 | -107.561 | 258214 | 3524882 | 1220.473 | 1158 | 31.82651 | -107.386 | 274177 | 3523500 | 1248.341 |
| 1128 | 31.8357 | -107.555 | 258825 | 3524869 | 1219.658 | 1159 | 31.82637 | -107.385 | 274278 | 3523481 | 1248.711 |
| 1129 | 31.83571 | -107.548 | 259448 | 3524835 | 1219.643 | 1160 | 31.82641 | -107.384 | 274380 | 3523484 | 1247.814 |
| 1130 | 31.83554 | -107.542 | 260047 | 3524869 | 1213.535 | 1161 | 31.82646 | -107.383 | 274482 | 3523487 | 1245.764 |
| 1131 | 31.83597 | -107.535 | 260620 | 3525003 | 1218.765 | 1162 | 31.82652 | -107.382 | 274582 | 3523491 | 1243.629 |
| 1132 | 31.8373 | -107.529 | 261191 | 3525328 | 1219.049 | 1163 | 31.82658 | -107.381 | 274683 | 3523496 | 1242.506 |
| 1133 | 31.84034 | -107.523 | 261883 | 3525439 | 1218.625 | 1164 | 31.82671 | -107.38 | 274783 | 3523508 | 1241.147 |
| 1134 | 31.84149 | -107.516 | 262426 | 3525441 | 1217.883 | 1165 | 31.82673 | -107.378 | 274884 | 3523508 | 1241.115 |
| 1135 | 31.84162 | -107.51 | 262981 | 3525330 | 1216.843 | 1166 | 31.82678 | -107.377 | 274984 | 3523512 | 1241.845 |
| 1136 | 31.84074 | -107.505 | 263646 | 3525210 | 1215.69 | 1167 | 31.82689 | -107.376 | 275085 | 3523522 | 1243.096 |
| 1137 | 31.8398 | -107.498 | 264259 | 3525110 | 1214.715 | 1168 | 31.82702 | -107.375 | 275184 | 3523534 | 1245.023 |
| 1138 | 31.83902 | -107.491 | 264840 | 3524978 | 1214.523 | 1169 | 31.82729 | -107.374 | 275281 | 3523562 | 1245.254 |
| 1139 | 31.83795 | -107.485 | 265432 | 3524869 | 1214.106 | 1170 | 31.82761 | -107.373 | 275374 | 3523596 | 1246.956 |
| 1140 | 31.83709 | -107.479 | 266001 | 3524757 | 1212.798 | 1171 | 31.82784 | -107.372 | 275473 | 3523618 | 1246.037 |
| 1141 | 31.8362 | -107.473 | 266623 | 3524646 | 1211.918 | 1172 | 31.82796 | -107.371 | 275573 | 3523629 | 1244.559 |
| 1142 | 31.83532 | -107.466 | 267221 | 3524525 | 1211.493 | 1173 | 31.82804 | -107.37 | 275675 | 3523636 | 1244.036 |
| 1143 | 31.83436 | -107.46 | 267799 | 3524322 | 1211.036 | 1174 | 31.82811 | -107.369 | 275775 | 3523642 | 1244.597 |
| 1144 | 31.83264 | -107.453 | 268424 | 3524000 | 1209.92 | 1175 | 31.82818 | -107.368 | 275873 | 3523647 | 1244.856 |
| 1145 | 31.82987 | -107.447 | 268974 | 3523720 | 1209.49 | 1176 | 31.82825 | -107.367 | 275974 | 3523653 | 1245.506 |
| 1177 | 31.82833 | -107.366 | 276074 | 3523659 | 1245.961 | 1207 | 31.83051 | -107.334 | 279077 | 3523837 | 1253.74 |
| 1178 | 31.8284 | -107.365 | 276175 | 3523665 | 1247.082 | 1208 | 31.83054 | -107.333 | 279177 | 3523837 | 1253.702 |
| 1179 | 31.82847 | -107.364 | 276275 | 3523671 | 1247.282 | 1209 | 31.83066 | -107.332 | 279276 | 3523849 | 1254.235 |
| 1180 | 31.82854 | -107.363 | 276375 | 3523677 | 1248.305 | 1210 | 31.83073 | -107.331 | 279376 | 3523855 | 1254.913 |
| 1181 | 31.82862 | -107.362 | 276475 | 3523683 | 1247.156 | 1211 | 31.83078 | -107.33 | 279476 | 3523858 | 1256.143 |
| 1182 | 31.82869 | -107.361 | 276575 | 3523689 | 1244.977 | 1212 | 31.83074 | -107.329 | 279576 | 3523852 | 1257.772 |
| 1183 | 31.82877 | -107.36 | 276675 | 3523695 | 1243.753 | 1213 | 31.8306 | -107.328 | 279675 | 3523834 | 1260.556 |
| 1184 | 31.82884 | -107.359 | 276776 | 3523701 | 1243.44 | 1214 | 31.83036 | -107.327 | 279789 | 3523805 | 1258.676 |
| 1185 | 31.82891 | -107.358 | 276876 | 3523707 | 1242.981 | 1215 | 31.83016 | -107.326 | 279881 | 3523781 | 1258.701 |
| 1186 | 31.82899 | -107.356 | 276976 | 3523713 | 1242.123 | 1216 | 31.82994 | -107.325 | 279985 | 3523754 | 1259.99 |
| 1187 | 31.82906 | -107.355 | 277076 | 3523719 | 1242.443 | 1217 | 31.82972 | -107.324 | 280090 | 3523727 | 1260.843 |
| 1188 | 31.82913 | -107.354 | 277176 | 3523725 | 1243.848 | 1218 | 31.8295 | -107.323 | 280189 | 3523701 | 1260.707 |
| 1189 | 31.82921 | -107.353 | 277276 | 3523731 | 1243.861 | 1219 | 31.82928 | -107.321 | 280291 | 3523674 | 1261.885 |
| 1190 | 31.82928 | -107.352 | 277376 | 3523737 | 1243.516 | 1220 | 31.82907 | -107.32 | 280392 | 3523649 | 1261.993 |
| 1191 | 31.82935 | -107.351 | 277476 | 3523743 | 1242.858 | 1221 | 31.82885 | -107.319 | 280490 | 3523623 | 1261.536 |
| 1192 | 31.82942 | -107.35 | 277576 | 3523749 | 1243.244 | 1222 | 31.82865 | -107.318 | 280588 | 3523597 | 1262.927 |
| 1193 | 31.8295 | -107.349 | 277676 | 3523755 | 1243.617 | 1223 | 31.82843 | -107.317 | 280686 | 3523572 | 1262.927 |
| 1194 | 31.82957 | -107.348 | 277776 | 3523760 | 1246.531 | 1224 | 31.82823 | -107.316 | 280784 | 3523547 | 1264.567 |
| 1195 | 31.82964 | -107.347 | 277876 | 3523766 | 1247.095 | 1225 | 31.82801 | -107.315 | 280885 | 3523521 | 1267.652 |
| 1196 | 31.82971 | -107.346 | 277977 | 3523772 | 1248.955 | 1226 | 31.8278 | -107.314 | 280984 | 3523495 | 1267.611 |
| 1197 | 31.82978 | -107.345 | 278077 | 3523778 | 1249.864 | 1227 | 31.82758 | -107.313 | 281083 | 3523469 | 1268.985 |
| 1198 | 31.82986 | -107.344 | 278177 | 3523783 | 1252.093 | 1228 | 31.82737 | -107.312 | 281182 | 3523444 | 1267.406 |
| 1199 | 31.82993 | -107.343 | 278277 | 3523789 | 1252.872 | 1229 | 31.82716 | -107.311 | 281279 | 3523418 | 1266.727 |
| 1200 | 31.83 | -107.342 | 278377 | 3523795 | 1252.657 | 1230 | 31.82695 | -107.31 | 281378 | 3523393 | 1267.671 |
| 1201 | 31.83007 | -107.341 | 278477 | 3523801 | 1252.481 | 1231 | 31.82674 | -107.309 | 281475 | 3523368 | 1268.12 |
| 1202 | 31.83015 | -107.34 | 278576 | 3523807 | 1251.723 | 1232 | 31.82654 | -107.308 | 281573 | 3523342 | 1268.569 |
| 1203 | 31.83022 | -107.339 | 278677 | 3523813 | 1252.65 | 1233 | 31.82633 | -107.307 | 281671 | 3523317 | 1269.387 |
| 1204 | 31.83029 | -107.337 | 278777 | 3523819 | 1253.514 | 1234 | 31.82612 | -107.306 | 281768 | 3523292 | 1269.1 |
| 1205 | 31.83037 | -107.336 | 278877 | 3523825 | 1253.657 | 1235 | 31.82591 | -107.305 | 281866 | 3523267 | 1269.621 |
| 1206 | 31.83044 | -107.335 | 278977 | 3523831 | 1252.989 | 1236 | 31.8257 | -107.304 | 281963 | 3523242 | 1269.9 |
| 1237 | 31.82549 | -107.303 | 282061 | 3523216 | 1269.806 | 1267 | 31.80226 | -107.259 | 286092 | 3520554 | 1256.181 |
| 1238 | 31.82528 | -107.302 | 282158 | 3523191 | 1266.566 | 1268 | 31.80135 | -107.258 | 286279 | 3520450 | 1259.094 |
| 1239 | 31.82507 | -107.301 | 282255 | 3523165 | 1263.272 | 1269 | 31.80069 | -107.255 | 286469 | 3520372 | 1257.724 |
| 1240 | 31.82486 | -107.3 | 282353 | 3523140 | 1262.32 | 1270 | 31.80001 | -107.253 | 286666 | 3520293 | 1259.877 |
| 1241 | 31.82465 | -107.298 | 282452 | 3523115 | 1264.901 | 1271 | 31.79933 | -107.251 | 286862 | 3520214 | 1258.06 |
| 1242 | 31.82444 | -107.297 | 282551 | 3523089 | 1263.712 | 1272 | 31.799 | -107.25 | 286957 | 3520175 | 1257.583 |
| 1243 | 31.82423 | -107.296 | 282648 | 3523064 | 1264.032 | 1273 | 31.79866 | -107.249 | 287053 | 3520136 | 1254.472 |
| 1244 | 31.82401 | -107.295 | 282746 | 3523038 | 1262.53 | 1274 | 31.79834 | -107.248 | 287147 | 3520097 | 1255.199 |
| 1245 | 31.82381 | -107.294 | 282844 | 3523013 | 1263.648 | 1275 | 31.79798 | -107.247 | 287248 | 3520056 | 1255.124 |
| 1246 | 31.8236 | -107.293 | 282941 | 3522988 | 1261.148 | 1276 | 31.79765 | -107.246 | 287346 | 3520017 | 1255.582 |
| 1247 | 31.82339 | -107.292 | 283039 | 3522963 | 1262.119 | 1277 | 31.79731 | -107.245 | 287443 | 3519978 | 1256.091 |
| 1248 | 31.82318 | -107.291 | 283136 | 3522937 | 1262.42 | 1278 | 31.79698 | -107.244 | 287540 | 3519938 | 1255.466 |
| 1249 | 31.82297 | -107.29 | 283234 | 3522912 | 1262.117 | 1279 | 31.79664 | -107.243 | 287639 | 3519899 | 1255.799 |
| 1250 | 31.82276 | -107.289 | 283332 | 3522887 | 1262.417 | 1280 | 31.7963 | -107.242 | 287734 | 3519860 | 1254.919 |
| 1251 | 31.82251 | -107.288 | 283428 | 3522856 | 1260.786 | 1281 | 31.79597 | -107.241 | 287830 | 3519821 | 1256.073 |
| 1252 | 31.82202 | -107.287 | 283534 | 3522800 | 1263.156 | 1282 | 31.79563 | -107.24 | 287929 | 3519782 | 1255.68 |
| 1253 | 31.82133 | -107.286 | 283634 | 3522721 | 1263.198 | 1283 | 31.7953 | -107.239 | 288024 | 3519743 | 1255.706 |
| 1254 | 31.82056 | -107.285 | 283730 | 3522634 | 1261.455 | 1284 | 31.79496 | -107.238 | 288123 | 3519703 | 1254.991 |
| 1255 | 31.81983 | -107.284 | 283826 | 3522550 | 1263.641 | 1285 | 31.79462 | -107.237 | 288220 | 3519664 | 1254.608 |
| 1256 | 31.81836 | -107.282 | 284014 | 3522384 | 1259.322 | 1286 | 31.79427 | -107.236 | 288321 | 3519622 | 1253.968 |
| 1257 | 31.8169 | -107.28 | 284201 | 3522218 | 1257.076 | 1287 | 31.79395 | -107.235 | 288415 | 3519585 | 1253.814 |
| 1258 | 31.81542 | -107.278 | 284392 | 3522050 | 1255.483 | 1288 | 31.79361 | -107.234 | 288511 | 3519545 | 1252.404 |
| 1259 | 31.81394 | -107.276 | 284582 | 3521882 | 1257.533 | 1289 | 31.79327 | -107.233 | 288609 | 3519506 | 1251.497 |
| 1260 | 31.81247 | -107.274 | 284770 | 3521715 | 1254.849 | 1290 | 31.79262 | -107.231 | 288802 | 3519429 | 1252.773 |
| 1261 | 31.81099 | -107.272 | 284959 | 3521546 | 1256.638 | 1291 | 31.79293 | -107.232 | 288708 | 3519466 | 1257.108 |
| 1262 | 31.80953 | -107.27 | 285147 | 3521381 | 1254.524 | 1292 | 31.79228 | -107.23 | 288900 | 3519389 | 1255.917 |
| 1263 | 31.80805 | -107.268 | 285336 | 3521213 | 1252.403 | 1293 | 31.79194 | -107.229 | 288997 | 3519350 | 1253.151 |
| 1264 | 31.80659 | -107.266 | 285525 | 3521046 | 1255.824 | 1294 | 31.7916 | -107.228 | 289094 | 3519311 | 1250.882 |
| 1265 | 31.80512 | -107.264 | 285714 | 3520879 | 1253.012 | 1295 | 31.79126 | -107.227 | 289192 | 3519271 | 1249.919 |
| 1266 | 31.80366 | -107.262 | 285900 | 3520714 | 1253.909 | 1296 | 31.79094 | -107.225 | 289290 | 3519233 | 1250.457 |
| 1297 | 31.79068 | -107.224 | 289388 | 3519202 | 1249.875 | 1327 | 31.78949 | -107.193 | 292379 | 3519010 | 1253.819 |
| 1298 | 31.79047 | -107.223 | 289486 | 3519177 | 1251.644 | 1328 | 31.78947 | -107.192 | 292478 | 3519005 | 1252.82 |
| 1299 | 31.79032 | -107.222 | 289584 | 3519159 | 1252.26 | 1329 | 31.78944 | -107.191 | 292579 | 3519000 | 1252.485 |
| 1300 | 31.79022 | -107.221 | 289685 | 3519146 | 1248.86 | 1330 | 31.78941 | -107.19 | 292679 | 3518995 | 1253.18 |
| 1301 | 31.79018 | -107.22 | 289785 | 3519138 | 1251.058 | 1331 | 31.78938 | -107.189 | 292779 | 3518990 | 1252.972 |
| 1302 | 31.79015 | -107.219 | 289885 | 3519133 | 1251.03 | 1332 | 31.78936 | -107.188 | 292878 | 3518985 | 1253.445 |
| 1303 | 31.79012 | -107.218 | 289986 | 3519128 | 1251.138 | 1333 | 31.78933 | -107.186 | 292978 | 3518980 | 1252.827 |
| 1304 | 31.7901 | -107.217 | 290086 | 3519123 | 1250.393 | 1334 | 31.78931 | -107.185 | 293078 | 3518975 | 1252.417 |
| 1305 | 31.79007 | -107.216 | 290185 | 3519119 | 1250.905 | 1335 | 31.78927 | -107.184 | 293182 | 3518969 | 1252.405 |
| 1306 | 31.79005 | -107.215 | 290284 | 3519114 | 1251.568 | 1336 | 31.78925 | -107.183 | 293281 | 3518965 | 1253.805 |
| 1307 | 31.79002 | -107.214 | 290386 | 3519109 | 1251.168 | 1337 | 31.78923 | -107.182 | 293380 | 3518960 | 1254.767 |
| 1308 | 31.78999 | -107.213 | 290486 | 3519104 | 1252.182 | 1338 | 31.7892 | -107.181 | 293479 | 3518955 | 1253.843 |
| 1309 | 31.78997 | -107.212 | 290586 | 3519099 | 1253.135 | 1339 | 31.78918 | -107.18 | 293579 | 3518950 | 1254.834 |
| 1310 | 31.78995 | -107.211 | 290687 | 3519094 | 1254.152 | 1340 | 31.78915 | -107.179 | 293678 | 3518945 | 1256.073 |
| 1311 | 31.78992 | -107.21 | 290787 | 3519089 | 1253.363 | 1341 | 31.78912 | -107.178 | 293777 | 3518941 | 1256.892 |
| 1312 | 31.78989 | -107.209 | 290887 | 3519084 | 1253.009 | 1342 | 31.7891 | -107.177 | 293876 | 3518936 | 1258.813 |
| 1313 | 31.78986 | -107.208 | 290988 | 3519079 | 1253.852 | 1343 | 31.78907 | -107.176 | 293977 | 3518931 | 1257.6 |
| 1314 | 31.78984 | -107.206 | 291088 | 3519074 | 1253.683 | 1344 | 31.78904 | -107.175 | 294077 | 3518926 | 1257.474 |
| 1315 | 31.78981 | -107.205 | 291189 | 3519068 | 1252.431 | 1345 | 31.78902 | -107.174 | 294177 | 3518921 | 1258.897 |
| 1316 | 31.78978 | -107.204 | 291290 | 3519063 | 1253.445 | 1346 | 31.78899 | -107.173 | 294277 | 3518916 | 1260.22 |
| 1317 | 31.78975 | -107.203 | 291389 | 3519058 | 1252.503 | 1347 | 31.78896 | -107.172 | 294378 | 3518911 | 1260.485 |
| 1318 | 31.78972 | -107.202 | 291489 | 3519053 | 1254.262 | 1348 | 31.78894 | -107.171 | 294477 | 3518906 | 1260.371 |
| 1319 | 31.78969 | -107.201 | 291588 | 3519048 | 1254.544 | 1349 | 31.78891 | -107.17 | 294577 | 3518901 | 1256.653 |
| 1320 | 31.78967 | -107.2 | 291686 | 3519043 | 1254.819 | 1350 | 31.78888 | -107.169 | 294677 | 3518896 | 1254.883 |
| 1321 | 31.78964 | -107.199 | 291785 | 3519039 | 1253.292 | 1351 | 31.7889 | -107.167 | 294778 | 3518896 | 1255.281 |
| 1322 | 31.78962 | -107.198 | 291884 | 3519034 | 1253.904 | 1352 | 31.789 | -107.166 | 294878 | 3518905 | 1257.283 |
| 1323 | 31.78959 | -107.197 | 291980 | 3519029 | 1253.967 | 1353 | 31.78917 | -107.165 | 294977 | 3518922 | 1258.273 |
| 1324 | 31.78956 | -107.196 | 292080 | 3519024 | 1254.164 | 1354 | 31.78945 | -107.164 | 295083 | 3518951 | 1256.914 |
| 1325 | 31.78955 | -107.195 | 292180 | 3519020 | 1252.932 | 1355 | 31.78984 | -107.163 | 295189 | 3518991 | 1259.126 |
| 1326 | 31.78952 | -107.194 | 292279 | 3519014 | 1254.382 | 1356 | 31.79025 | -107.162 | 295293 | 3519035 | 1255.425 |
| 1358 | 31.79107 | -107.16 | 295498 | 3519122 | 1254.361 | 1388 | 31.80039 | -107.128 | 298585 | 3520095 | 1248.214 |
| 1359 | 31.79149 | -107.159 | 295602 | 3519166 | 1254.603 | 1389 | 31.80068 | -107.126 | 298689 | 3520125 | 1247.545 |
| 1360 | 31.79191 | -107.158 | 295708 | 3519211 | 1253.05 | 1390 | 31.80097 | -107.125 | 298792 | 3520155 | 1245.491 |
| 1361 | 31.79231 | -107.157 | 295807 | 3519253 | 1253.476 | 1391 | 31.80125 | -107.124 | 298893 | 3520184 | 1246.398 |
| 1362 | 31.79272 | -107.156 | 295912 | 3519297 | 1253.453 | 1392 | 31.80154 | -107.123 | 298997 | 3520214 | 1246.205 |
| 1363 | 31.79313 | -107.154 | 296015 | 3519341 | 1253.706 | 1393 | 31.80182 | -107.122 | 299097 | 3520244 | 1246.383 |
| 1364 | 31.79349 | -107.153 | 296119 | 3519378 | 1249.06 | 1394 | 31.80211 | -107.121 | 299201 | 3520274 | 1244.356 |
| 1365 | 31.79373 | -107.152 | 296215 | 3519403 | 1247.77 | 1395 | 31.80239 | -107.12 | 299302 | 3520303 | 1244.446 |
| 1366 | 31.79407 | -107.151 | 296322 | 3519438 | 1248.316 | 1396 | 31.80266 | -107.119 | 299406 | 3520331 | 1245.498 |
| 1367 | 31.79436 | -107.15 | 296425 | 3519468 | 1248.021 | 1397 | 31.80284 | -107.118 | 299507 | 3520349 | 1242.982 |
| 1368 | 31.79465 | -107.149 | 296530 | 3519499 | 1247.589 | 1398 | 31.80295 | -107.117 | 299611 | 3520359 | 1241.851 |
| 1369 | 31.79493 | -107.148 | 296632 | 3519528 | 1246.94 | 1399 | 31.80297 | -107.116 | 299708 | 3520359 | 1240.245 |
| 1370 | 31.79522 | -107.147 | 296736 | 3519558 | 1245.559 | 1400 | 31.80292 | -107.115 | 299808 | 3520352 | 1240.194 |
| 1371 | 31.79551 | -107.146 | 296838 | 3519588 | 1245.219 | 1401 | 31.80279 | -107.114 | 299908 | 3520335 | 1244.684 |
| 1372 | 31.7958 | -107.145 | 296942 | 3519618 | 1245.535 | 1402 | 31.80264 | -107.113 | 300006 | 3520317 | 1241.691 |
| 1373 | 31.79609 | -107.144 | 297047 | 3519648 | 1245.404 | 1403 | 31.80249 | -107.112 | 300106 | 3520298 | 1242.573 |
| 1374 | 31.79638 | -107.143 | 297149 | 3519678 | 1244.901 | 1404 | 31.80234 | -107.11 | 300205 | 3520279 | 1242.177 |
| 1375 | 31.79666 | -107.142 | 297249 | 3519707 | 1244.521 | 1405 | 31.80222 | -107.109 | 300304 | 3520264 | 1243.563 |
| 1376 | 31.79695 | -107.14 | 297354 | 3519738 | 1244.683 | 1406 | 31.80232 | -107.108 | 300402 | 3520273 | 1246.196 |
| 1377 | 31.79724 | -107.139 | 297457 | 3519767 | 1246.391 | 1407 | 31.80274 | -107.107 | 300499 | 3520318 | 1239.845 |
| 1378 | 31.79752 | -107.138 | 297558 | 3519797 | 1246.947 | 1408 | 31.80354 | -107.106 | 300616 | 3520405 | 1240.932 |
| 1379 | 31.7978 | -107.137 | 297660 | 3519826 | 1246.372 | 1409 | 31.80427 | -107.105 | 300720 | 3520484 | 1237.582 |
| 1380 | 31.7981 | -107.136 | 297765 | 3519857 | 1245.579 | 1410 | 31.80504 | -107.104 | 300829 | 3520567 | 1235.24 |
| 1381 | 31.79838 | -107.135 | 297866 | 3519886 | 1244.614 | 1411 | 31.80578 | -107.103 | 300920 | 3520647 | 1235.381 |
| 1382 | 31.79867 | -107.134 | 297971 | 3519917 | 1245.17 | 1412 | 31.80696 | -107.102 | 301044 | 3520776 | 1235.821 |
| 1383 | 31.79896 | -107.133 | 298074 | 3519947 | 1244.76 | 1413 | 31.80817 | -107.101 | 301151 | 3520907 | 1236.829 |
| 1384 | 31.79924 | -107.132 | 298173 | 3519976 | 1244.178 | 1414 | 31.8094 | -107.099 | 301258 | 3521043 | 1240.58 |
| 1385 | 31.79953 | -107.131 | 298276 | 3520005 | 1246.55 | 1415 | 31.81067 | -107.098 | 301369 | 3521181 | 1241.228 |
| 1386 | 31.79981 | -107.13 | 298378 | 3520034 | 1248.08 | 1416 | 31.81195 | -107.097 | 301478 | 3521320 | 1242.115 |
| 1387 | 31.8001 | -107.129 | 298482 | 3520065 | 1249.703 | 1417 | 31.81321 | -107.096 | 301588 | 3521458 | 1243.387 |
| 1418 | 31.81446 | -107.095 | 301697 | 3521595 | 1247.066 | 1448 | 31.81424 | -107.063 | 304702 | 3521513 | 1252.082 |
| 1419 | 31.81567 | -107.094 | 301808 | 3521727 | 1247.86 | 1449 | 31.81411 | -107.062 | 304802 | 3521497 | 1252.646 |
| 1420 | 31.8166 | -107.093 | 301916 | 3521828 | 1249.565 | 1450 | 31.81396 | -107.061 | 304900 | 3521479 | 1252.732 |
| 1421 | 31.81707 | -107.092 | 302017 | 3521879 | 1256.827 | 1451 | 31.81378 | -107.06 | 304999 | 3521456 | 1255.468 |
| 1422 | 31.81735 | -107.091 | 302120 | 3521908 | 1254.038 | 1452 | 31.81353 | -107.059 | 305099 | 3521427 | 1256.806 |
| 1423 | 31.81744 | -107.09 | 302221 | 3521915 | 1252.984 | 1453 | 31.81326 | -107.058 | 305195 | 3521396 | 1257.827 |
| 1424 | 31.81735 | -107.088 | 302322 | 3521903 | 1253.252 | 1454 | 31.813 | -107.057 | 305293 | 3521364 | 1259.512 |
| 1425 | 31.81722 | -107.087 | 302423 | 3521887 | 1252.829 | 1455 | 31.81273 | -107.056 | 305391 | 3521333 | 1260.129 |
| 1426 | 31.81693 | -107.086 | 302521 | 3521853 | 1252.882 | 1456 | 31.81247 | -107.055 | 305488 | 3521302 | 1261.002 |
| 1427 | 31.81687 | -107.085 | 302621 | 3521844 | 1252.454 | 1457 | 31.8122 | -107.054 | 305588 | 3521270 | 1262.933 |
| 1428 | 31.81668 | -107.084 | 302720 | 3521822 | 1253.441 | 1458 | 31.81194 | -107.053 | 305685 | 3521239 | 1265.296 |
| 1429 | 31.81669 | -107.083 | 302821 | 3521821 | 1253.187 | 1459 | 31.81167 | -107.052 | 305783 | 3521207 | 1266.024 |
| 1430 | 31.81657 | -107.082 | 302918 | 3521805 | 1253.169 | 1460 | 31.8114 | -107.051 | 305882 | 3521176 | 1266.017 |
| 1431 | 31.81644 | -107.081 | 303017 | 3521789 | 1253.217 | 1461 | 31.81114 | -107.05 | 305980 | 3521145 | 1265.969 |
| 1432 | 31.81631 | -107.08 | 303116 | 3521773 | 1251.954 | 1462 | 31.81087 | -107.049 | 306080 | 3521113 | 1269.196 |
| 1433 | 31.81618 | -107.079 | 303214 | 3521757 | 1252.252 | 1463 | 31.8106 | -107.048 | 306178 | 3521081 | 1268.1 |
| 1434 | 31.81605 | -107.078 | 303315 | 3521740 | 1253.033 | 1464 | 31.81033 | -107.047 | 306276 | 3521050 | 1267.161 |
| 1435 | 31.81592 | -107.077 | 303414 | 3521724 | 1253.229 | 1465 | 31.81006 | -107.045 | 306375 | 3521018 | 1267.859 |
| 1436 | 31.81578 | -107.076 | 303513 | 3521707 | 1251.851 | 1466 | 31.8098 | -107.044 | 306473 | 3520987 | 1265.58 |
| 1437 | 31.81566 | -107.075 | 303613 | 3521692 | 1252.39 | 1467 | 31.80953 | -107.043 | 306571 | 3520956 | 1264.046 |
| 1438 | 31.81553 | -107.074 | 303711 | 3521676 | 1252.212 | 1468 | 31.80926 | -107.042 | 306669 | 3520924 | 1264.276 |
| 1439 | 31.8154 | -107.073 | 303812 | 3521659 | 1251.258 | 1469 | 31.809 | -107.041 | 306768 | 3520893 | 1263.651 |
| 1440 | 31.81528 | -107.072 | 303910 | 3521643 | 1252.097 | 1470 | 31.80873 | -107.04 | 306865 | 3520861 | 1264.288 |
| 1441 | 31.81514 | -107.071 | 304009 | 3521627 | 1251.747 | 1471 | 31.80846 | -107.039 | 306964 | 3520830 | 1265.056 |
| 1442 | 31.81502 | -107.07 | 304108 | 3521610 | 1252.239 | 1472 | 31.8082 | -107.038 | 307062 | 3520798 | 1266.271 |
| 1443 | 31.81488 | -107.068 | 304207 | 3521594 | 1252.92 | 1473 | 31.80793 | -107.037 | 307160 | 3520767 | 1267.03 |
| 1444 | 31.81475 | -107.067 | 304307 | 3521577 | 1253.727 | 1474 | 31.80767 | -107.036 | 307258 | 3520736 | 1267.146 |
| 1445 | 31.81462 | -107.066 | 304405 | 3521561 | 1253.893 | 1475 | 31.80739 | -107.035 | 307356 | 3520704 | 1267.841 |
| 1446 | 31.81449 | -107.065 | 304505 | 3521545 | 1253.247 | 1476 | 31.80713 | -107.034 | 307454 | 3520673 | 1267.691 |
| 1447 | 31.81437 | -107.064 | 304603 | 3521529 | 1252.853 | 1477 | 31.80687 | -107.033 | 307552 | 3520642 | 1268.333 |
| 1478 | 31.80661 | -107.032 | 307650 | 3520611 | 1270.256 | 1508 | 31.80123 | -107.001 | 310611 | 3519960 | 1289.096 |
| 1479 | 31.80634 | -107.031 | 307748 | 3520580 | 1270.688 | 1509 | 31.80123 | -106.999 | 310710 | 3519958 | 1291.998 |
| 1480 | 31.80608 | -107.03 | 307846 | 3520549 | 1271.799 | 1510 | 31.80124 | -106.998 | 310810 | 3519957 | 1292.57 |
| 1481 | 31.80581 | -107.029 | 307944 | 3520518 | 1271.908 | 1511 | 31.80124 | -106.997 | 310910 | 3519956 | 1293.071 |
| 1482 | 31.80555 | -107.028 | 308042 | 3520486 | 1273.306 | 1512 | 31.80125 | -106.996 | 311009 | 3519955 | 1291.936 |
| 1483 | 31.80528 | -107.027 | 308140 | 3520455 | 1272.218 | 1513 | 31.80125 | -106.995 | 311111 | 3519953 | 1292.949 |
| 1484 | 31.80502 | -107.026 | 308236 | 3520424 | 1270.161 | 1514 | 31.80126 | -106.994 | 311210 | 3519952 | 1293.61 |
| 1485 | 31.80475 | -107.025 | 308335 | 3520392 | 1270.198 | 1515 | 31.80128 | -106.993 | 311311 | 3519952 | 1294.152 |
| 1486 | 31.80449 | -107.024 | 308433 | 3520361 | 1270.425 | 1516 | 31.80133 | -106.992 | 311412 | 3519956 | 1296.49 |
| 1487 | 31.80422 | -107.023 | 308530 | 3520330 | 1272.385 | 1517 | 31.8014 | -106.991 | 311512 | 3519963 | 1295.826 |
| 1488 | 31.80396 | -107.022 | 308628 | 3520299 | 1273.81 | 1518 | 31.80149 | -106.99 | 311612 | 3519970 | 1295.022 |
| 1489 | 31.80369 | -107.02 | 308727 | 3520267 | 1273.401 | 1519 | 31.80168 | -106.988 | 311814 | 3519988 | 1294.346 |
| 1490 | 31.80343 | -107.019 | 308824 | 3520237 | 1273.148 | 1520 | 31.80187 | -106.986 | 312016 | 3520005 | 1293.96 |
| 1491 | 31.80316 | -107.018 | 308922 | 3520205 | 1273.912 | 1521 | 31.80205 | -106.984 | 312219 | 3520022 | 1291.769 |
| 1492 | 31.80289 | -107.017 | 309020 | 3520174 | 1273.794 | 1522 | 31.80223 | -106.981 | 312420 | 3520038 | 1290.141 |
| 1493 | 31.80262 | -107.016 | 309119 | 3520142 | 1274.506 | 1523 | 31.80242 | -106.979 | 312622 | 3520055 | 1288.073 |
| 1494 | 31.80226 | -107.015 | 309215 | 3520099 | 1276.564 | 1524 | 31.80254 | -106.977 | 312824 | 3520065 | 1287.59 |
| 1495 | 31.80199 | -107.014 | 309316 | 3520068 | 1280.316 | 1525 | 31.80186 | -106.975 | 313018 | 3519986 | 1283.975 |
| 1496 | 31.80183 | -107.013 | 309414 | 3520048 | 1279.999 | 1526 | 31.79955 | -106.973 | 313201 | 3519726 | 1280.885 |
| 1497 | 31.80155 | -107.012 | 309513 | 3520016 | 1282.33 | 1527 | 31.79682 | -106.971 | 313379 | 3519420 | 1278.739 |
| 1498 | 31.80133 | -107.011 | 309611 | 3519989 | 1282.462 | 1528 | 31.79448 | -106.969 | 313560 | 3519157 | 1276.709 |
| 1499 | 31.80121 | -107.01 | 309710 | 3519974 | 1283.196 | 1529 | 31.79356 | -106.967 | 313758 | 3519052 | 1273.435 |
| 1500 | 31.80118 | -107.009 | 309810 | 3519970 | 1282.298 | 1530 | 31.79352 | -106.965 | 313957 | 3519044 | 1271.707 |
| 1501 | 31.80119 | -107.008 | 309910 | 3519969 | 1283.631 | 1531 | 31.79375 | -106.963 | 314156 | 3519066 | 1269.771 |
| 1502 | 31.8012 | -107.007 | 310010 | 3519967 | 1285.092 | 1532 | 31.79398 | -106.961 | 314356 | 3519088 | 1269.172 |
| 1503 | 31.8012 | -107.006 | 310109 | 3519966 | 1285.062 | 1533 | 31.79422 | -106.959 | 314558 | 3519110 | 1269.464 |
| 1504 | 31.80121 | -107.005 | 310210 | 3519965 | 1289.563 | 1534 | 31.79445 | -106.957 | 314762 | 3519132 | 1269.412 |
| 1505 | 31.80121 | -107.004 | 310309 | 3519963 | 1287.724 | 1535 | 31.79457 | -106.955 | 314863 | 3519143 | 1269.594 |
| 1506 | 31.80122 | -107.003 | 310410 | 3519963 | 1291.569 | 1536 | 31.79468 | -106.954 | 314964 | 3519154 | 1268.98 |
| 1507 | 31.80122 | -107.002 | 310509 | 3519961 | 1291.349 | 1537 | 31.79479 | -106.953 | 315065 | 3519165 | 1268.551 |
| 1538 | 31.79491 | -106.952 | 315166 | 3519176 | 1268.161 | 1568 | 31.79836 | -106.92 | 318195 | 3519505 | 1260.591 |
| 1539 | 31.79502 | -106.951 | 315268 | 3519187 | 1267.829 | 1569 | 31.79848 | -106.919 | 318298 | 3519516 | 1260.886 |
| 1540 | 31.79514 | -106.95 | 315369 | 3519198 | 1267.841 | 1570 | 31.7986 | -106.918 | 318399 | 3519527 | 1260.792 |
| 1541 | 31.79525 | -106.949 | 315470 | 3519209 | 1267.318 | 1571 | 31.79871 | -106.917 | 318500 | 3519538 | 1260.107 |
| 1542 | 31.79537 | -106.948 | 315571 | 3519220 | 1266.748 | 1572 | 31.79882 | -106.916 | 318600 | 3519549 | 1259.158 |
| 1543 | 31.79548 | -106.947 | 315671 | 3519231 | 1266.321 | 1573 | 31.79894 | -106.915 | 318701 | 3519560 | 1260.365 |
| 1544 | 31.7956 | -106.946 | 315772 | 3519242 | 1266.058 | 1574 | 31.79905 | -106.914 | 318801 | 3519571 | 1260.379 |
| 1545 | 31.79572 | -106.945 | 315873 | 3519253 | 1265.794 | 1575 | 31.79917 | -106.913 | 318903 | 3519582 | 1259.722 |
| 1546 | 31.79583 | -106.944 | 315974 | 3519264 | 1265.206 | 1576 | 31.79928 | -106.912 | 319004 | 3519593 | 1259.435 |
| 1547 | 31.79595 | -106.943 | 316075 | 3519275 | 1264.602 | 1577 | 31.7994 | -106.911 | 319106 | 3519604 | 1259.48 |
| 1548 | 31.79606 | -106.942 | 316176 | 3519286 | 1264.757 | 1578 | 31.79951 | -106.91 | 319207 | 3519615 | 1258.677 |
| 1549 | 31.79618 | -106.941 | 316277 | 3519297 | 1264.171 | 1579 | 31.79963 | -106.909 | 319308 | 3519626 | 1258.618 |
| 1550 | 31.79629 | -106.94 | 316378 | 3519308 | 1264.59 | 1580 | 31.79974 | -106.908 | 319409 | 3519637 | 1258.169 |
| 1551 | 31.79641 | -106.938 | 316478 | 3519319 | 1264.906 | 1581 | 31.79986 | -106.907 | 319510 | 3519647 | 1256.444 |
| 1552 | 31.79653 | -106.937 | 316579 | 3519330 | 1265.087 | 1582 | 31.79997 | -106.905 | 319611 | 3519659 | 1255.077 |
| 1553 | 31.79664 | -106.936 | 316680 | 3519341 | 1265.029 | 1583 | 31.80009 | -106.904 | 319713 | 3519670 | 1256.671 |
| 1554 | 31.79676 | -106.935 | 316781 | 3519352 | 1265.399 | 1584 | 31.8002 | -106.903 | 319813 | 3519681 | 1256.845 |
| 1555 | 31.79687 | -106.934 | 316882 | 3519363 | 1264.955 | 1585 | 31.80032 | -106.902 | 319914 | 3519692 | 1255.539 |
| 1556 | 31.79699 | -106.933 | 316983 | 3519374 | 1264.542 | 1586 | 31.80043 | -106.901 | 320015 | 3519703 | 1254.084 |
| 1557 | 31.7971 | -106.932 | 317084 | 3519385 | 1263.049 | 1587 | 31.80055 | -106.9 | 320116 | 3519713 | 1254.058 |
| 1558 | 31.79722 | -106.931 | 317186 | 3519396 | 1263.012 | 1588 | 31.80066 | -106.899 | 320217 | 3519725 | 1254.701 |
| 1559 | 31.79733 | -106.93 | 317287 | 3519407 | 1262.546 | 1589 | 31.80078 | -106.898 | 320317 | 3519736 | 1255.366 |
| 1560 | 31.79745 | -106.929 | 317388 | 3519418 | 1262.577 | 1590 | 31.80089 | -106.897 | 320418 | 3519747 | 1255.488 |
| 1561 | 31.79756 | -106.928 | 317489 | 3519429 | 1260.925 | 1591 | 31.80101 | -106.896 | 320520 | 3519757 | 1257.419 |
| 1562 | 31.79767 | -106.927 | 317590 | 3519439 | 1258.352 | 1592 | 31.80112 | -106.895 | 320621 | 3519768 | 1258.867 |
| 1563 | 31.79778 | -106.926 | 317689 | 3519450 | 1255.422 | 1593 | 31.80124 | -106.894 | 320721 | 3519779 | 1259.407 |
| 1564 | 31.7979 | -106.925 | 317791 | 3519461 | 1258.36 | 1594 | 31.80135 | -106.893 | 320823 | 3519790 | 1259.628 |
| 1565 | 31.79802 | -106.924 | 317893 | 3519472 | 1258.755 | 1595 | 31.80147 | -106.892 | 320924 | 3519801 | 1260.126 |
| 1566 | 31.79813 | -106.923 | 317993 | 3519483 | 1261.227 | 1596 | 31.80158 | -106.891 | 321024 | 3519812 | 1257.94 |
| 1567 | 31.79825 | -106.921 | 318094 | 3519494 | 1260.828 | 1597 | 31.80169 | -106.89 | 321125 | 3519823 | 1258.3 |
| 1598 | 31.8018 | -106.888 | 321224 | 3519834 | 1259.295 | 1628 | 31.80525 | -106.857 | 324255 | 3520163 | 1255.509 |
| 1599 | 31.80192 | -106.887 | 321327 | 3519845 | 1258.813 | 1629 | 31.80536 | -106.855 | 324355 | 3520174 | 1255.862 |
| 1600 | 31.802 | -106.886 | 321428 | 3519852 | 1257.992 | 1630 | 31.80548 | -106.854 | 324456 | 3520185 | 1256.805 |
| 1601 | 31.80215 | -106.885 | 321530 | 3519867 | 1258.974 | 1631 | 31.80559 | -106.853 | 324557 | 3520196 | 1257.882 |
| 1602 | 31.80227 | -106.884 | 321632 | 3519878 | 1258.233 | 1632 | 31.80571 | -106.852 | 324658 | 3520207 | 1258.858 |
| 1603 | 31.80239 | -106.883 | 321732 | 3519889 | 1258.399 | 1633 | 31.80582 | -106.851 | 324759 | 3520218 | 1259.908 |
| 1604 | 31.8025 | -106.882 | 321833 | 3519900 | 1257.361 | 1634 | 31.80593 | -106.85 | 324859 | 3520229 | 1260.052 |
| 1605 | 31.80262 | -106.881 | 321933 | 3519911 | 1256.616 | 1635 | 31.80605 | -106.849 | 324959 | 3520240 | 1259.717 |
| 1606 | 31.80273 | -106.88 | 322035 | 3519922 | 1257.472 | 1636 | 31.80616 | -106.848 | 325060 | 3520251 | 1260.638 |
| 1607 | 31.80284 | -106.879 | 322134 | 3519933 | 1256.103 | 1637 | 31.80628 | -106.847 | 325161 | 3520262 | 1260.7 |
| 1608 | 31.80296 | -106.878 | 322235 | 3519944 | 1255.751 | 1638 | 31.8064 | -106.846 | 325263 | 3520273 | 1259.921 |
| 1609 | 31.80308 | -106.877 | 322337 | 3519955 | 1255.496 | 1639 | 31.80651 | -106.845 | 325363 | 3520284 | 1259.418 |
| 1610 | 31.80319 | -106.876 | 322436 | 3519966 | 1256.577 | 1640 | 31.80663 | -106.844 | 325463 | 3520296 | 1257.617 |
| 1611 | 31.8033 | -106.875 | 322537 | 3519977 | 1257.191 | 1641 | 31.80674 | -106.843 | 325564 | 3520306 | 1257.409 |
| 1612 | 31.80342 | -106.874 | 322638 | 3519988 | 1257.545 | 1642 | 31.80685 | -106.842 | 325664 | 3520317 | 1257.017 |
| 1613 | 31.80354 | -106.872 | 322739 | 3519999 | 1258.036 | 1643 | 31.80697 | -106.841 | 325764 | 3520328 | 1257.458 |
| 1614 | 31.80364 | -106.871 | 322840 | 3520010 | 1257.362 | 1644 | 31.80708 | -106.84 | 325866 | 3520339 | 1256.967 |
| 1615 | 31.80376 | -106.87 | 322941 | 3520021 | 1257.741 | 1645 | 31.80719 | -106.838 | 325967 | 3520350 | 1256.551 |
| 1616 | 31.80382 | -106.869 | 323043 | 3520026 | 1257.379 | 1646 | 31.80731 | -106.837 | 326069 | 3520361 | 1256.414 |
| 1617 | 31.80399 | -106.868 | 323144 | 3520043 | 1256.876 | 1647 | 31.80742 | -106.836 | 326170 | 3520372 | 1256.64 |
| 1618 | 31.8041 | -106.867 | 323245 | 3520054 | 1256.853 | 1648 | 31.80754 | -106.835 | 326271 | 3520383 | 1256.642 |
| 1619 | 31.80422 | -106.866 | 323347 | 3520065 | 1256.385 | 1649 | 31.80765 | -106.834 | 326372 | 3520394 | 1256.496 |
| 1620 | 31.80434 | -106.865 | 323448 | 3520076 | 1257.095 | 1650 | 31.80777 | -106.833 | 326473 | 3520405 | 1257.817 |
| 1621 | 31.80445 | -106.864 | 323549 | 3520087 | 1257.255 | 1651 | 31.80788 | -106.832 | 326575 | 3520416 | 1257.045 |
| 1622 | 31.80456 | -106.863 | 323650 | 3520098 | 1257.894 | 1652 | 31.808 | -106.831 | 326675 | 3520427 | 1257.501 |
| 1623 | 31.80468 | -106.862 | 323753 | 3520109 | 1258.241 | 1653 | 31.80811 | -106.83 | 326775 | 3520438 | 1258.063 |
| 1624 | 31.80479 | -106.861 | 323852 | 3520120 | 1257.9 | 1654 | 31.80822 | -106.829 | 326877 | 3520449 | 1258.136 |
| 1625 | 31.80491 | -106.86 | 323953 | 3520131 | 1257.746 | 1655 | 31.80834 | -106.828 | 326978 | 3520460 | 1258.86 |
| 1626 | 31.80502 | -106.859 | 324053 | 3520142 | 1257.888 | 1656 | 31.80845 | -106.827 | 327079 | 3520471 | 1259.497 |
| 1627 | 31.80513 | -106.858 | 324155 | 3520152 | 1256.39 | 1657 | 31.80857 | -106.826 | 327179 | 3520482 | 1258.266 |
| 1658 | 31.80868 | -106.825 | 327277 | 3520492 | 1258.327 | 1688 | 31.82521 | -106.665 | 342399 | 3522083 | 1247.756 |
| 1659 | 31.80878 | -106.824 | 327371 | 3520503 | 1258.197 | 1689 | 31.82595 | -106.659 | 343010 | 3522156 | 1251.68 |
| 1660 | 31.80889 | -106.823 | 327466 | 3520513 | 1255.364 | 1690 | 31.82631 | -106.653 | 343597 | 3522186 | 1253.094 |
| 1661 | 31.80895 | -106.822 | 327566 | 3520518 | 1255.409 | 1691 | 31.82524 | -106.646 | 344185 | 3522059 | 1251.647 |
| 1662 | 31.80908 | -106.821 | 327663 | 3520531 | 1255.917 | 1692 | 31.82382 | -106.64 | 344786 | 3521892 | 1245.512 |
| 1663 | 31.80924 | -106.819 | 327779 | 3520547 | 1255.231 | 1693 | 31.82206 | -106.633 | 345417 | 3521688 | 1236.483 |
| 1664 | 31.80931 | -106.818 | 327889 | 3520552 | 1254.339 | 1694 | 31.82137 | -106.627 | 345985 | 3521603 | 1209.233 |
| 1665 | 31.80999 | -106.812 | 328491 | 3520617 | 1256.339 | 1695 | 31.82112 | -106.621 | 346590 | 3521566 | 1198.406 |
| 1666 | 31.81065 | -106.805 | 329100 | 3520680 | 1255.47 | 1696 | 31.82097 | -106.615 | 347176 | 3521541 | 1188.268 |
| 1667 | 31.81137 | -106.799 | 329692 | 3520751 | 1258.361 | 1697 | 31.82084 | -106.608 | 347781 | 3521517 | 1170.594 |
| 1668 | 31.81208 | -106.793 | 330284 | 3520820 | 1255.548 | 1698 | 31.82082 | -106.602 | 348376 | 3521506 | 1158.463 |
| 1669 | 31.81274 | -106.786 | 330908 | 3520883 | 1254.172 | 1699 | 31.82141 | -106.595 | 348995 | 3521563 | 1142.294 |
| 1670 | 31.81344 | -106.78 | 331516 | 3520951 | 1251.923 | 1700 | 31.82226 | -106.589 | 349592 | 3521648 | 1141.416 |
| 1671 | 31.81412 | -106.774 | 332124 | 3521015 | 1250.139 | 1701 | 31.82237 | -106.583 | 350202 | 3521652 | 1141.341 |
| 1672 | 31.81474 | -106.767 | 332755 | 3521075 | 1250.226 | 1702 | 31.82243 | -106.577 | 350790 | 3521650 | 1141.247 |
| 1673 | 31.81551 | -106.761 | 333332 | 3521150 | 1250.808 | 1703 | 31.8216 | -106.57 | 351384 | 3521548 | 1140.691 |
| 1674 | 31.81605 | -106.755 | 333930 | 3521201 | 1248.919 | 1704 | 31.82153 | -106.564 | 351990 | 3521532 | 1141.668 |
| 1675 | 31.81674 | -106.748 | 334540 | 3521267 | 1247.521 | 1705 | 31.82101 | -106.558 | 352588 | 3521465 | 1151.278 |
| 1676 | 31.81751 | -106.742 | 335145 | 3521343 | 1246.015 | 1706 | 31.82095 | -106.551 | 353174 | 3521450 | 1168.902 |
| 1677 | 31.81814 | -106.735 | 335740 | 3521403 | 1245.891 | 1707 | 31.82168 | -106.545 | 353792 | 3521523 | 1189.757 |
| 1678 | 31.81882 | -106.729 | 336348 | 3521468 | 1243.73 | 1708 | 31.82149 | -106.538 | 354390 | 3521493 | 1196.46 |
| 1679 | 31.81954 | -106.723 | 336933 | 3521539 | 1244.862 | 1709 | 31.82052 | -106.533 | 354947 | 3521352 | 1219.536 |
| 1680 | 31.82026 | -106.716 | 337562 | 3521610 | 1246.662 | 1710 | 31.8202 | -106.526 | 355586 | 3521334 | 1238.987 |
| 1681 | 31.82091 | -106.71 | 338156 | 3521672 | 1250.203 | 1711 | 31.82005 | -106.52 | 356170 | 3521308 | 1243.147 |
| 1682 | 31.82155 | -106.704 | 338754 | 3521734 | 1251.626 | 1712 | 31.82091 | -106.513 | 356766 | 3521396 | 1314.698 |
| 1683 | 31.82219 | -106.698 | 339330 | 3521795 | 1252.556 | 1713 | 31.82224 | -106.507 | 357384 | 3521535 | 1323.13 |
| 1684 | 31.82292 | -106.691 | 339956 | 3521866 | 1251.678 | 1714 | 31.82182 | -106.5 | 357991 | 3521479 | 1412.397 |
| 1685 | 31.8232 | -106.684 | 340654 | 3521887 | 1251.95 | 1715 | 31.82314 | -106.481 | 359800 | 3521601 | 1453.202 |
| 1686 | 31.82399 | -106.678 | 341193 | 3521965 | 1252.089 | 1716 | 31.82255 | -106.475 | 360400 | 3521528 | 1373.603 |
| 1687 | 31.82461 | -106.672 | 341798 | 3522026 | 1247.702 | 1717 | 31.82261 | -106.469 | 361002 | 3521526 | 1310.468 |
| 1718 | 31.82415 | -106.462 | 361661 | 3521688 | 1275.008 | 1749 | 31.85011 | -106.316 | 375521 | 3524389 | 1218.898 |
| 1719 | 31.82431 | -106.456 | 362212 | 3521698 | 1252.789 | 1750 | 31.84993 | -106.314 | 375721 | 3524366 | 1220.193 |
| 1720 | 31.82497 | -106.45 | 362800 | 3521763 | 1221.612 | 1751 | 31.84998 | -106.311 | 375921 | 3524369 | 1220.018 |
| 1721 | 31.82533 | -106.443 | 363416 | 3521795 | 1200.038 | 1752 | 31.84994 | -106.309 | 376125 | 3524363 | 1218.758 |
| 1723 | 31.82565 | -106.43 | 364632 | 3521815 | 1180.278 | 1753 | 31.84994 | -106.307 | 376327 | 3524361 | 1217.197 |
| 1724 | 31.82591 | -106.424 | 365205 | 3521836 | 1181.175 | 1754 | 31.85014 | -106.305 | 376522 | 3524380 | 1217.104 |
| 1725 | 31.82592 | -106.417 | 365874 | 3521828 | 1182.158 | 1755 | 31.85012 | -106.303 | 376721 | 3524376 | 1218.642 |
| 1726 | 31.82589 | -106.412 | 366415 | 3521818 | 1185.844 | 1756 | 31.85029 | -106.301 | 376925 | 3524391 | 1218.968 |
| 1727 | 31.82553 | -106.405 | 367010 | 3521770 | 1189.466 | 1757 | 31.85061 | -106.299 | 377125 | 3524425 | 1218.429 |
| 1728 | 31.82626 | -106.399 | 367605 | 3521844 | 1192.867 | 1758 | 31.85087 | -106.297 | 377328 | 3524451 | 1213.303 |
| 1729 | 31.82639 | -106.393 | 368212 | 3521850 | 1193.807 | 1759 | 31.85123 | -106.294 | 377530 | 3524489 | 1212.917 |
| 1730 | 31.82649 | -106.386 | 368828 | 3521853 | 1194.734 | 1760 | 31.85151 | -106.292 | 377732 | 3524518 | 1214.642 |
| 1731 | 31.82661 | -106.38 | 369418 | 3521859 | 1197.989 | 1761 | 31.85181 | -106.29 | 377930 | 3524548 | 1219.164 |
| 1732 | 31.82717 | -106.373 | 370019 | 3521914 | 1201.46 | 1762 | 31.85199 | -106.288 | 378136 | 3524566 | 1220.754 |
| 1733 | 31.82714 | -106.368 | 370577 | 3521903 | 1203.58 | 1763 | 31.85245 | -106.286 | 378330 | 3524614 | 1222.802 |
| 1734 | 31.8323 | -106.36 | 371255 | 3522467 | 1201.611 | 1764 | 31.85288 | -106.284 | 378535 | 3524660 | 1226.688 |
| 1735 | 31.8369 | -106.354 | 371862 | 3522970 | 1198.087 | 1765 | 31.85286 | -106.282 | 378732 | 3524655 | 1221.638 |
| 1736 | 31.84159 | -106.348 | 372443 | 3523482 | 1198.879 | 1766 | 31.85279 | -106.28 | 378931 | 3524645 | 1219.682 |
| 1737 | 31.84633 | -106.341 | 373096 | 3523999 | 1206.557 | 1767 | 31.85393 | -106.277 | 379143 | 3524769 | 1219.042 |
| 1738 | 31.84709 | -106.339 | 373312 | 3524081 | 1206.684 | 1768 | 31.8557 | -106.275 | 379347 | 3524963 | 1221.443 |
| 1739 | 31.84797 | -106.337 | 373509 | 3524176 | 1208.227 | 1769 | 31.8574 | -106.273 | 379549 | 3525149 | 1222.626 |
| 1740 | 31.84886 | -106.335 | 373707 | 3524272 | 1209.372 | 1770 | 31.85918 | -106.271 | 379759 | 3525343 | 1225.381 |
| 1741 | 31.84986 | -106.333 | 373902 | 3524380 | 1210.575 | 1771 | 31.86091 | -106.269 | 379966 | 3525533 | 1226.382 |
| 1742 | 31.85082 | -106.331 | 374102 | 3524485 | 1211.677 | 1772 | 31.86277 | -106.267 | 380169 | 3525737 | 1225.379 |
| 1743 | 31.84861 | -106.328 | 374323 | 3524477 | 1210.098 | 1773 | 31.86429 | -106.265 | 380371 | 3525903 | 1227.283 |
| 1744 | 31.8488 | -106.326 | 374514 | 3524418 | 1211.024 | 1774 | 31.8662 | -106.262 | 380579 | 3526112 | 1228.611 |
| 1745 | 31.84914 | -106.324 | 374715 | 3524387 | 1213.564 | 1775 | 31.86797 | -106.26 | 380780 | 3526306 | 1227.683 |
| 1746 | 31.84956 | -106.322 | 374919 | 3524386 | 1215.323 | 1776 | 31.8698 | -106.258 | 380990 | 3526507 | 1224.358 |
| 1747 | 31.85004 | -106.32 | 375123 | 3524386 | 1215.28 | 1777 | 31.87121 | -106.256 | 381191 | 3526660 | 1218.678 |
| 1748 | 31.85043 | -106.318 | 375324 | 3524427 | 1217.751 | 1778 | 31.87227 | -106.254 | 381395 | 3526776 | 1220.211 |
| 1779 | 31.87312 | -106.252 | 381598 | 3526868 | 1222.362 |  |  |  |  |  |  |
| 1780 | 31.874 | -106.25 | 381801 | 3526963 | 1221.735 |  |  |  |  |  |  |
| 1781 | 31.87479 | -106.247 | 382003 | 3527048 | 1224.175 |  |  |  |  |  |  |
| 1782 | 31.87562 | -106.245 | 382204 | 3527138 | 1225.393 |  |  |  |  |  |  |
| 1783 | 31.87644 | -106.243 | 382404 | 3527226 | 1227.543 |  |  |  |  |  |  |
| 1784 | 31.8773 | -106.241 | 382611 | 3527319 | 1226.418 |  |  |  |  |  |  |
| 1785 | 31.87814 | -106.239 | 382810 | 3527410 | 1227.845 |  |  |  |  |  |  |
| 1786 | 31.87902 | -106.237 | 383011 | 3527506 | 1229.823 |  |  |  |  |  |  |
| 1787 | 31.87985 | -106.235 | 383214 | 3527596 | 1231.008 |  |  |  |  |  |  |
| 1788 | 31.8806 | -106.233 | 383409 | 3527676 | 1229.566 |  |  |  |  |  |  |
| 1789 | 31.88158 | -106.23 | 383618 | 3527783 | 1231.341 |  |  |  |  |  |  |
| 1790 | 31.88243 | -106.228 | 383819 | 3527875 | 1233.164 |  |  |  |  |  |  |
| 1791 | 31.88318 | -106.226 | 384020 | 3527956 | 1233.898 |  |  |  |  |  |  |
| 1792 | 31.88407 | -106.224 | 384222 | 3528052 | 1234.389 |  |  |  |  |  |  |
| 1793 | 31.88491 | -106.222 | 384425 | 3528143 | 1236.483 |  |  |  |  |  |  |
| 1794 | 31.88581 | -106.22 | 384626 | 3528241 | 1235.415 |  |  |  |  |  |  |
| 1795 | 31.88664 | -106.218 | 384827 | 3528330 | 1235.589 |  |  |  |  |  |  |

*  Stations 1001 - 1058  UTM zone 12

*  Stations 1059 - 1795  UTM zone 13

# TABLE 3:  SEGY TRACE HEADER VALUES USED FOR PVF SEGYTAPES

| Bytes | Format | SEGY name | PVF Header |
| --- | --- | --- | --- |
| 1-4 | integer | TRACENO | Trace number (1-7137) |
| 9-12 | integer | FFID | Shot sequence number (1-9) |
| 13-16 | integer | CHAN | Channel # (1-793) |
| 17-20 | integer | SOURCE | Shot station number |
| 37-40 | integer | OFFSET | Source-receiver distance (m) |
| 41-44 | integer | REC_ELEV | Receiver elevation (m) |
| 45-48 | integer | SOU_ELEV | Source elevation (m) |
| 73-76 | integer | SOU_X | X coordinate for source (arcsec longitude) |
| 77-80 | integer | SOU_Y | Y coordinate for source (arcsec latitude) |
| 81-84 | integer | REC_X | X coordinate for receiver (arcsec longitude) |
| 85-88 | integer | REC_Y | Y coordinate for receiver (arcsec latitude) |
| 103-104 | int*2 | stat_corr | Clock drift correction |
| 115-116 | int*4 | strace | Samples per trace |
| 117-118 | int*5 | sint | Sample rate |
| 157-158 | int*6 | year | year |
| 159-160 | int*7 | day | day |
| 161-162 | int*8 | hour | hour |
| 163-164 | int*9 | minute | minute |
| 165-166 | int*10 | second | second |
| 167-168 | int*11 | tbasis | time basis (2=GMT) |
| 173-174 | int*12 | instrno | Instrument number |
| 181-184 | float | SOU_UTMN | Source location (UTM meters Northing) |
| 185-188 | float | SOU_UTME | Source location (UTM meters Easting) |
| 189-192 | float | REC_UTMN | Receiver location (UTM meters Northing) |
| 193-196 | float | REC_UTME | Receiver location (UTM meters Easting) |
| 197-200 | float | STATION | Station number in field (1001-1795) |
| 201-204 | float | box_no | Box number |