## Slide 1: Real-time Waveform Data Exchange

## Slide 2: Real-time Data Exchange
Allows automated integration of external data into network operations
Convenient automated data sharing if data is already collected in real-time
Streamline data collection and archiving operations (e.g. at the IRIS DMC)

## Slide 3: Real-time Data Exchange
 | Earthworm | SeedLink (SeisComP) | NRTS/ISI | LISS | Antelope | NAQS | Scream!
Earthworm |  | Yes |  | Yes | Yes |  | 
SeedLink (SeisComP) | Yes |  |  | Possible | Yes | Yes | 
NRTS/ISI | Yes | Yes |  |  | Yes |  | 
LISS | Yes | Yes |  |  | Yes |  | 
Antelope | Yes | Yes |  |  |  |  | 
NAQS | Yes | Yes |  |  |  |  | 
Scream! | Yes | Yes |  |  |  |  | 
A number of open-source and commercial data exchange systems exist, the bridges between them are illustrated below.

## Slide 4: Free Real-time Processing and Exchange
SeisComP: Complete seismic network operations and data exchange (SeedLink and ArcLink)
Earthworm: Complete seismic network operations and data exchange (tracebuf and wavetank/Winston)
Standalone SeedLink server (DMC)

## Slide 5: Real-time Data from the IRIS DMC
SeedLink
host: rtserve.iris.washington.edu
port: 18000 (default)
* All data in this server is openly available.