## Slide 1: Waveform Data Exchange

## Slide 2: The challenges of data exchange
Data format
  SEED, IMS/GSE, SAC, SeisAn, CSS, proprietary
Protocol
  SeedLink, Earthworm, HTTP, FTP, Antelope ORB, etc.
Network connectivity
  Internet, intranet, firewalls
Non-technical issues
  Politics
Notes: IRIS makes many tools available for dealing with SEED and Mini-SEED

## Slide 3: Real-time Data Exchange
 | Earthworm | SeisComP/ SeedLink | ISI/NRTS | LISS | Antelope | NAQS | Scream!
Earthworm |  | Yes |  | Yes | Yes |  | 
SeisComP/ SeedLink | Yes |  |  | Possible | Yes | Yes? | 
ISI/NRTS | Yes | Yes |  |  | Yes |  | 
LISS | Yes | Yes |  |  | Yes |  | 
Antelope | Yes | Yes |  |  |  |  | 
NAQS | Yes | Yes |  |  |  |  | 
Scream! | Yes | Yes |  |  |  |  | 
A number of open-source and commercial data exchange systems exist, the bridges between them are illustrated below.

## Slide 4: Submitting non-real-time data to IRIS
miniseed2dmc: A dedicated program for submitting batches of Mini-SEED data directly to the IRIS DMC.
Robustly transmits data to the DMC, tolerant of network disconnects and transmission restarts
Designed to transmit very large data sets
Reports transmission summary
Dataless SEED metadata must be supplied separately
Distributed as source code, a C compiler is required
Coordination with the IRIS DMC is required before submitting data.

## Slide 5: Real-time data from the IRIS DMC
All open data received at the IRIS DMC is publicly available in real-time using the SeedLink protocol.
Host: rtserve.iris.washington.edu
Port: 18000 (default SeedLink port)
For more details visit:
http://www.iris.edu/data/dmc-seedlink.htm

## Slide 6: Ringserver: a stand alone SeedLink server
The IRIS DMC’s SeedLink implementation is available for use by others. Any data center creating 512-byte Mini-SEED records can have a SeedLink server.
Source code:
http://www.iris.edu/pub/programs/ringserver/
SeedLink server configuration instructions:
HowTo-SeedLink-server.txt (at above address)
* ringserver is not a replacement for SeisComP, SeisComP plugins are not compatible with ringserver

## Slide 7: Highlights of ringserver implementation
Stateful and self-correcting operation
Extremely scalable threaded architecture
Ring buffer is First In First Out (FIFO)
Buffer size & number of clients limited only by hardware
Dynamic configuration file options
Control access by IP address, limit access at stream level
SeedLink 3.1 plus Network and Station wildcarding
Comprehensive transfer logging
Runs on Linux, Mac OSX and Solaris (32 and 64-bit )
Integrated Mini-SEED file system scanner

## Slide 8: Ringserver as a simple SeedLink server
512-byte
Mini-SEED
files
SeisComP
slarchive
slink2orb
slink2ew
NAQS
…
Ringserver
Internal buffer of data

## Slide 9: Ringserver installation
  Read the HowTo-SeedLink-server.txt document
  General steps:
  Download and compile ringserver source code (C)
  Create ringserver configuration, identify directories to scan for Mini-SEED data files
  Execute ringserver independently or from an automated system
  Use dalitool or slinktool to verify that data is flowing as expected

## Slide 10: Ringserver related software
dalitool – General purpose ringserver query
  Report server ID, version, general status, transfer rate
  List connected clients and associated stats
  Data stream inspection
dali2liss – Create LISS servers from ringserver streams
slink2dali – Send SeedLink streams to ringserver (beta)
mseedscan2dali – Alternate Mini-SEED scanner