## Slide 1: Portable Data Collection Center (PDCC) and the Nominal Response Library (NRL)
Tim Ahern

## Slide 2: PDCC – creation of dataless SEED
SEED
  metadata contains both simple and complex informatio
  format is difficult to build and edit correctly
PDCC
  was designed to simplify the task of building metadata to describe your seismic stations/channels
  can also be used to edit existing dataless SEED volumes
  is a client application that runs in a terminal window
    Java so runs on most operating systems

## Slide 3: Hierarchical Structure of SEED components
Standard for Exchange of Earthquake Data (SEED) Volumes contain two parts
  Dataless SEED volume
    Networks
      Two character network code
    Stations
      Five character station names
    Location Identifiers
      Two character without required convention
    Channels
      Three character channel codes
  Data only SEED or miniSEED

## Slide 4: PDCC startup window

## Slide 5: To get started
Create a new dataless SEED volume
Launch Build a Station
  Enter Station Code and Network ID
    Answer a variety of questions about network and station
    Latitude, Longitude, and Elevation and Depth
    Define Instrumentation
      Using NRL tool
      Specify Configuration of Sensor at Station
        Manufacturer and configuration
        The information must match configuration of actual station in the field

## Slide 6: PDCC displays a RESP file after the sensor is fully specified identified

## Slide 7: Next select and specify datalogger configuration PDCC will display the RESP file for the data logger

## Slide 8: NRL (http://www.iris.edu/NRL)
Directories each have an index.txt file that enables logical navigation of the NRL
[Main]
  question = "Select the hardware category”
[Sensor]
  path = "sensors/index.txt”
[Datalogger]
  path = "dataloggers/index.txt"

## Slide 9: Selecting sensor
[Main]
  question = "Select the sensor manufacturer”
[CEA-DASE]
  path = "dase/index.txt”
[Eentec]
  path = "eentec/index.txt”
[Geotech]
  path = "geotech/index.txt”
[Guralp]
  path = "guralp/index.txt”
[Kinemetrics]
  path = "kinemetrics/index.txt”
[Lennartz]
  path = "lennartz/index.txt"

## Slide 10: Selecting Sensor Continued
[Nanometrics]
  path = "nanometrics/index.txt”
[OYO Geospace]
  path = "oyo_geospace/index.txt”
[REF TEK]
  path = "reftek/index.txt”
[Sercel/Mark Products]
  path = "sercel/index.txt”
[Streckeisen]
  path = "streckeisen/index.txt”
[Generic]
  path = "generic/index.txt"

## Slide 11: If one selects Streckeisen for instance
[Main]
  question = "Select the Streckeisen sensor model”
[STS-1]
  path = "sts-1.txt”
[STS-2]
  path = "sts-2.txt"

## Slide 12: STS-2 specific configuration
[Main]
  question = "Select the sensor sensitivity in V/m/s”
[1500]
  path = "sts-2.1500.txt”
[20000]
  path = "sts-2.20000.txt"
There can be many, many questions required to specify
The configuration at your seismic station

## Slide 13: Sensor specification continued
[Main]
  question = "Select the generation of electronics used in this STS-2"
  detail = "streckeisen_sts2_sensors-details.html”
[1 - installed 01/90 to 09/94]
  resp = "RESP.XX.NS081..BHZ.STS2_gen1.120.1500"
  description = "STS-2, 120 s, 1500 V/m/s, generation 1 electronics”
[2 - installed 09/94 to 04/97]
  resp = "RESP.XX.NS083..BHZ.STS2_gen2.120.1500"
  description = "STS-2, 120 s, 1500 V/m/s, generation 2 electronics”
[3 - installed 04/97 to present]
  resp = "RESP.XX.NS085..BHZ.STS2_gen3.120.1500"
  description = "STS-2, 120 s, 1500 V/m/s, generation 3 electronics"

## Slide 14: RESP File Produced
Stage 1
Poles & Zeroes
Gain

## Slide 15: RESP file continued
Stage 2
Units
Sample Rate
Gain
Stage 0
Overall Gain

## Slide 16: NRL could be used directly but
A utility called “NRL Tool” can be launched from within PDCC to make the navigation of the NRL directories simpler
This provides an easy to use GUI to help describe the seismic stations

## Slide 17: Describe the first station completely
Then use Clone Station Tool to duplicate stations of similar configuration
  Change things such as
    Latitude, longitude, site name, elevation, depth, etc

## Slide 18: The Goal
The goal at this workshop is for each of you to be able to produce the metadata that describes actual stations in your network
Focus will be on hands-on use of PDCC