## Slide 1: Station Metadata and a little about the future of miniseed
TIM AHERN, DIRECTOR, IRIS DATA SERVICES

## Slide 2: What is in a SEED volume?
A SEED volume has two components that are usually transmitted in separate files.
  Time series data
    sometimes referred to as
      dataonly SEED or
      miniSEED
  The metadata needed to understand the time series data
    Referred to as a dataless SEED volume or
    A StationXML file

## Slide 3: Metadata
The dataless SEED or StationXML contains the information to understand and fully use the time series data
Key components
  Station location
  Type of instrumentation (digitizer and sensors)
  Response to ground motion (or physical parameter)
  Network DOIs, etc.

## Slide 4: Tools to build station metadata
Building the metadata files is not simple but it is essential
There are very few tools to build station metadata from scratch
  Most are based on the Nominal Response Library (NRL) maintained by IRIS’ Mary Templeton
  Known NRL examples
    Station Information System/US Regional Nets
    Portable Data Collection Center (PDCC)/IRIS
    Nexus built upon ObsPy/IRIS PASSCAL
    GEMPA web tool, requires user account
  Other commercial systems exist
    Antelope from BRTT
    Nanometrics
    Etc.
  We will introduce you to PDCC in this workshop
    Some from the ESARSWG group were introduced to this in December of 2015

## Slide 5: What about miniSEED
miniSEED2 has existed from its original version in February 1988 with minor changes
  Version 2.1 March, 1990
    Several blockette were added
  Version 2.2 August, 1991
    2 additional blockettes introduced
    Concept of dataless SEED volumes introduced
  Version 2.3 December 1992
    Several blockettes added to deal with new situations
    Concept of miniSEED or dataonly SEED introduced
  Latest version 2.4 April 2004
    Introduction of introduction of data quality indicator field

## Slide 6: IRIS is now developing miniSEED3
Working with several FDSN partners
Primary motivation is to support larger number of channels in a given network or temporary deployment
Data can be converted from miniSEED2 to miniSEED3 without loss of information
Networks not needing these new capabilities can continue using miniSEED2