## Slide 1: IRIS QA Network Reports – Finding Issues
Specifics of how we use MUSTANG to identify data and instrument issues

## Slide 2
QA Reports
Concept: different issues can be identified by using different metrics in combination
dead_channel_lin
pct_below_nlnm
num_gaps
num_spikes
sample_rms
pct_above_nhnm
sample_rms
IU.QSPA.60.BH2
IU.FURI.00.BH1
review

## Slide 3
Concept: scripts can call the web services and combine values based on defined criteria
By setting up scripts to combine the metrics for us, we can automate the process of “issue finding”
There are likely to be false positives, so the issues should be reviewed
This can only pick up issues that are catchable by MUSTANG metrics – we have a decent list at this point, but are always happy to hear about new metrics or thresholds that could be useful
QA Reports
review

## Slide 4
The Scripts We Use
  There are a few scripts that we use that we are making available to you
  One is the “work horse” – it grabs all of the metrics and combines them
  One generates the actual HTML report
  The rest are used to facilitate the process from start to finish
I’m going to go through these in some detail so that they can be used or adapted to your needs.
QA Reports
doQA

## Slide 5
Overview GUI (doQA.py)
Facilitates start-to-finish of reporting process
Python
Preference file or manual input
Autofills based on date. Reporting period for last month
Path to preference file
If no preference file, then need to fill in these fields
Run the scripts
QA Reports
doQA

## Slide 6
Process:
Find Issues
Evaluate Issues
Generate Report
Process:
Find Issues
Evaluate Issues
Generate Report
Use MUSTANG web services to retrieve measurements
Manual review of PDFs
Combine different metrics to find different issues
QA Reports
overview

## Slide 7
Finding Issues
“Work horse”
Python code
Web services
Preference file optional
Find Issues
Preference
File
Thresholds
Issue List
Report Utilities
Find Issues
OR: python findIssues.py --start=2018-06-01 --end=2018-07-01 --preference_file=/path/to/preference.py --network=IU --stations=* --channels=BH?,HH? --locations=* --outfile=/path/to/report.orig
QA Reports

## Slide 8
findIssues.py
Find Issues
Preference
File
Thresholds
Issue List
Report Utilities
Goes through the list of threshold “Groups”
Grabs metrics required for all thresholds in that group
Subsets based on listed thresholds
Writes offenders to outfile
QA Reports – Finding Issues
Find Issues

## Slide 9
Find Issues
Preference
File
Thresholds
Issue List
Report Utilities
thresholds.py
This is where you can change threshold definitions
Requires: pandas, reportUtils.py
Each threshold is its own defined function
  Ex: runGapsRatioGt12
Instrument types are defined by channel names
  channelDict = {"broadband" : ['BH?','HH*'], "short period" : ["EH*","SH*"]}
QA Reports – Finding Issues
Find Issues

## Slide 10
Find Issues
Preference
File
Thresholds
Issue List
Report Utilities
preference.py
Preference file is used to define:
SNCL information
Threshold Groups
Directory and name for outfile
This is useful for when QA may be done separately on different channel groups or networks.
Ex. Some stations may not have any timing information, while others do. To prevent cluttering the outfile, they can be divided into two separate preference files.
QA Reports – Finding Issues
Find Issues

## Slide 11
Find Issues
Preference
File
Thresholds
Issue List
Report Utilities
reportUtils.py
This is where the utility work happens
Parses input arguments
Grabs metrics through web services
Combines metrics as defined in thresholds.py
Sorts and writes outfile
Requires: pandas, numpy, datetime, argparse, sys
QA Reports – Finding Issues
Find Issues

## Slide 12
Find Issues
Preference
File
Thresholds
Issue List
Report Utilities
issueFile.orig
List of issues sorted by threshold
Pipe separated
Threshold|Target|Start|End|Ndays|Status|Notes
These fields different for some thresholds, which are averages over the reporting period.
For example, avgGaps has no start or end associated, and reports the average value rather than the number of days.
This file isn’t very human readable, but is easily parsed by QuARG.py
QA Reports – Finding Issues
Find Issues

## Slide 13
findIssues.py
Find Issues
Preference
File
Thresholds
Issue List
Report Utilities
When run, it will output progress to the console:
QA Reports – Finding Issues
Find Issues

## Slide 14
QA Reports – Finding Issues
Use findIssues.py to highlight problem sncl-days using MUSTANG metrics
  The preference file can be used to more easily refine searches or switch between searches, reduces the number of inputs
  The threshold definitions can be viewed or changed in thresholds.py
  reportUtils.py has the functions that grab and combine metrics, amongst other things
  This produces a file (by default report.orig) that isn’t easily human readable but is used in the next step to examine issues.
You can use the GUI doQA.py to easily load in files and autofill from there
  OR
You can run findIssues.py on the command line
Recap